## Slide 1
Lesson 17
PIO: Hardware WS2812 Driver
Fundamentals of C++ for Microcontrollers | Module 4
Programmable I/O | State Machines | RP2350 Exclusive Feature

## Slide 2
Lesson 17 | PIO: Hardware WS2812 Driver
2
The Problem with Bit-Banging
Bit-Bang Limitations
CPU is 100% busy during transmission
Must disable interrupts (blocks Serial, USB, timers)
Timing depends on compiler optimization
Cannot do anything else while sending
Scales poorly: 100+ LEDs = long CPU lockout
PIO Solution
Dedicated hardware generates the signal
CPU is free to do other work
Interrupts stay enabled
Cycle-exact timing, no jitter
Scales to hundreds of LEDs effortlessly

## Slide 3
Lesson 17 | PIO: Hardware WS2812 Driver
3
What Is PIO?
Programmable I/O -- tiny programmable state machines built into the RP2040/RP2350 chip. They run independently of the CPU and can implement custom I/O protocols in hardware.
PIO Blocks
3 (RP2350)
2 (RP2040)
State Machines
4 per block
12 total
Instruction Mem
32 instructions
per block
Clock Speed
Up to system
clock (150 MHz)

## Slide 4
Lesson 17 | PIO: Hardware WS2812 Driver
4
PIO Architecture
CPU
(Cortex-M33)
push
TX FIFO
(4 x 32-bit)
pull
RX FIFO
(4 x 32-bit)
State Machine
OSR (Output Shift Reg)
ISR (Input Shift Reg)
X, Y scratch registers
PC (program counter)
Clock divider
GPIO
Pins
Instruction Memory (32 words, shared by 4 SMs)
CPU writes pixel data to TX FIFO. State machine shifts bits out to GPIO with exact timing. CPU is free.

## Slide 5
Lesson 17 | PIO: Hardware WS2812 Driver
5
PIO Instruction Set (9 Instructions)
Instruction | Description | Used for WS2812?
jmp | Jump (conditional/unconditional) | Yes
pull | Load word from TX FIFO into OSR | Yes
out | Shift bits from OSR to pins/X/Y | Yes
set | Write immediate value to pins/X/Y | Yes
nop | No operation (delay only) | Yes (via side-set)
push | Write ISR to RX FIFO | No
in | Shift bits into ISR from pins | No
mov | Copy between registers | No
wait | Stall until pin/IRQ condition | No
Each instruction also has optional side-set (toggle pins) and delay (wait N cycles)

## Slide 6
Lesson 17 | PIO: Hardware WS2812 Driver
6
Key Concept: Side-Set & Delay
Side-Set
Toggle GPIO pins as a side effect of any instruction
Example: out x, 1 side 1
= shift 1 bit into X AND set pin HIGH simultaneously
Delay
Wait N extra cycles after instruction executes
Example: nop [5]
= do nothing, then wait 5 more cycles
Why This Matters for WS2812
Side-set lets us toggle the data pin HIGH/LOW at exact cycle boundaries, while the main instruction handles data shifting. Delays fine-tune the pulse widths to match WS2812 timing specs (T0H, T1H, T0L, T1L).

## Slide 7
Lesson 17 | PIO: Hardware WS2812 Driver
7
The WS2812 PIO Program
.program ws2812
.side_set 1
.wrap_target
bitloop:
out x, 1 side 0 [T3]
jmp !x do_zero side 1 [T1]
do_one:
jmp bitloop side 1 [T2]
do_zero:
nop side 0 [T2]
.wrap
How It Works
1
Pull 1 bit from OSR into X, set pin LOW (start of cycle)
2
If bit=0, jump to do_zero; set pin HIGH (start of pulse)
3
Bit=1: stay HIGH longer, then loop back
4
Bit=0: go LOW early, wait, then loop back
Only 4 instructions! The side-set and delays do all the timing work.

## Slide 8
Lesson 17 | PIO: Hardware WS2812 Driver
8
PIO Timing: How the Pulses Form
Bit "1"
LOW
out x,1
side 0 [T3]
HIGH
jmp !x
side 1 [T1]
HIGH
jmp bitloop
side 1 [T2]
Total HIGH = T1 + T2 + 2 cycles (long pulse = bit 1)
Bit "0"
LOW
out x,1
side 0 [T3]
HIGH
jmp !x
side 1 [T1]
LOW
nop
side 0 [T2]
Total HIGH = T1 + 1 cycle only (short pulse = bit 0)

## Slide 9
Lesson 17 | PIO: Hardware WS2812 Driver
9
C Code: Loading & Using the PIO
// 1. Choose PIO block and find a free SM
PIO pio = pio0;
uint sm = pio_claim_unused_sm(pio, true);
// 2. Add the compiled PIO program
uint offset = pio_add_program(pio, &ws2812_program);
// 3. Configure the state machine
ws2812_program_init(pio, sm, offset, WS2812_PIN);
// 4. Send pixel data -- just write to the FIFO!
void put_pixel(uint32_t grb) {
pio_sm_put_blocking(pio, sm, grb << 8);
}
// Usage: put_pixel(0x00FF00); // Green

## Slide 10
Lesson 17 | PIO: Hardware WS2812 Driver
10
Bit-Bang vs PIO: Comparison
Aspect | Bit-Bang (L16) | PIO (L17)
CPU Usage | 100% during send | ~0% (FIFO write only)
Interrupts | Must disable | Stay enabled
Timing Accuracy | Depends on compiler | Cycle-exact
Scalability | Poor (>100 LEDs = lag) | Excellent
Code Complexity | Simple C | PIO assembly needed
Portability | Any MCU | RP2040/RP2350 only
Learning Value | Protocol understanding | Hardware offloading
Both are valid tools -- bit-bang for learning, PIO for production

## Slide 11
Lesson 17 | PIO: Hardware WS2812 Driver
11
PIO Beyond WS2812
PIO can implement almost any digital I/O protocol:
VGA / DVI Video
Drive a display directly from PIO pins
Extra UART / SPI / I2C
Add more serial ports beyond hardware limits
Parallel Bus (8080)
Drive LCDs with parallel interfaces
Rotary Encoders
Quadrature decoding without CPU polling
Logic Analyzer
Capture signals at up to system clock rate
Audio I2S / PDM
Digital audio in/out for microphones, DACs
PIO is the killer feature that sets RP2040/RP2350 apart from ESP32 and STM32

## Slide 12
Homework & RP2350 Wrap-Up
Homework
Refactor Lesson 16 ring effects to use PIO driver
Compare: measure CPU time with bit-bang vs PIO (use a GPIO toggle as probe)
Bonus: drive two independent LED strips on two different PIO state machines simultaneously
Bonus: add a 4th animation effect using your creativity
Coming Up
Cross-Platform Comparison:
ESP32-C3 vs STM32 vs RP2350
GPIO, peripherals, ecosystem
When to choose which platform
Trade-offs and sweet spots
Push your project to GitHub Classroom before next session