## Slide 1
MODULE 2 · LESSON 9
Creating Peripheral
Control Libraries
ESP32-C3 · C++ · PlatformIO · drivers::
DigitalPin AnalogPin PwmPin Button Led

## Slide 2
Why Abstract Hardware?
Without abstraction
// setup()
pinMode(3, OUTPUT);
ledcSetup(0, 5000, 8);
ledcAttachPin(3, 0);
pinMode(0, INPUT_PULLUP);
attachInterrupt(0, isr0, CHANGE);
// scattered everywhere...
ledcWrite(0, 128);
if (!digitalRead(0)) { ... }
With drivers:: library
// main.cpp
drivers::Led red(3);
drivers::Button btn(0);
// loop()
if (btn.isPressed()) {
red.setDutyCycle(128);
}
Single responsibility
Reusable across projects
Easy to test & swap

## Slide 3
Library Architecture
project/
include/
digital_pin.h
analog_pin.h
pwm_pin.h
button.h
led.h
src/
button.cpp
led.cpp
main.cpp
namespace drivers::
Wrap ALL classes — prevents name collisions
.h in include/
Declarations only — no method bodies
.cpp in src/
Implementations — #include their own header
#pragma once
Include guard — always, in every header
No Arduino.h
in .h files — include only in .cpp

## Slide 4
DigitalPin — GPIO Abstraction Base
// include/digital_pin.h
#pragma once
#include <stdint.h>
namespace drivers {
class DigitalPin {
public:
explicit DigitalPin(uint8_t pin, uint8_t mode);
~DigitalPin(); // RAII: cleanup
void write(bool high);
bool read() const;
uint8_t pin() const;
protected:
uint8_t _pin;
uint8_t _mode;
};
} // namespace drivers
RAII
Constructor calls pinMode()
Destructor can detach interrupts
explicit
Prevents implicit int->DigitalPin
conversions — always good practice
protected
Derived classes (Button, Led)
need access to _pin and _mode
const read()
Marking read() const lets the
compiler catch accidental writes

## Slide 5
AnalogPin — analogRead Wrapper
// include/analog_pin.h
#pragma once
#include <stdint.h>
namespace drivers {
class AnalogPin {
public:
explicit AnalogPin(uint8_t pin);
uint16_t read() const; // raw 0-4095
float readVolt() const; // 0.0 - 3.3 V
uint8_t pin() const;
private:
uint8_t _pin;
};
} // namespace drivers
ESP32-C3 ADC facts
12-bit resolution
0 – 4095 counts
Reference voltage
3.3 V (VDD)
ADC1 only
GPIO0–GPIO4 (ADC1_CH0–CH4)
ADC2 disabled
shared with Wi-Fi — avoid
readVolt() formula
raw / 4095.0f * 3.3f
float readVolt() const {
return analogRead(_pin) / 4095.0f * 3.3f;
}

## Slide 6
PwmPin — LEDC Wrapper
// include/pwm_pin.h
#pragma once
#include <stdint.h>
namespace drivers {
class PwmPin {
public:
PwmPin(uint8_t pin, uint8_t channel,
uint32_t freq = 5000,
uint8_t bits = 8);
~PwmPin();
void setDutyCycle(uint8_t duty); // 0-255
private:
uint8_t _pin;
uint8_t _channel;
uint32_t _freq;
uint8_t _bits;
};
} // namespace drivers
LEDC recap (Arduino Core 2.x)
ledcSetup(ch, freq, bits);
ledcAttachPin(pin, ch);
ledcWrite(ch, duty);
Channel strategy
ESP32-C3 has 6 LEDC channels (0–5)
Pass channel explicitly — caller decides
Each PwmPin owns one channel for its lifetime
Destructor calls ledcDetachPin()

## Slide 7
Class Hierarchy
DigitalPin (base)
- _pin: uint8_t
- _mode: uint8_t
+ write(bool)
+ read() const
+ pin() const
PwmPin (base)
- _channel: uint8_t
- _freq: uint32_t
- _bits: uint8_t
+ setDutyCycle(uint8_t)
+ ~PwmPin()
Button : DigitalPin
- _lastState: bool
- _lastMs: uint32_t
+ isPressed() const
+ IRAM_ATTR onISR()
Led : DigitalPin, PwmPin
- _duty: uint8_t
- _fadeTarget: uint8_t
+ on() / off() / toggle()
+ setDutyCycle() / fade() update()
inherits
inherits (multiple)

## Slide 8
Button — ISR + Debounce
// include/button.h
#pragma once
#include "digital_pin.h"
namespace drivers {
class Button : public DigitalPin {
public:
explicit Button(uint8_t pin);
bool isPressed() const;
void IRAM_ATTR onISR();
private:
volatile bool _pressed;
volatile uint32_t _lastMs;
static const uint32_t DEBOUNCE_MS = 50;
};
} // namespace drivers
// src/button.cpp
#include "button.h"
#include <Arduino.h>
namespace drivers {
Button::Button(uint8_t pin)
: DigitalPin(pin, INPUT_PULLUP)
, _pressed(false), _lastMs(0) {}
bool Button::isPressed() const {
return _pressed;
}
void IRAM_ATTR Button::onISR() {
uint32_t now = millis();
if (now - _lastMs < DEBOUNCE_MS) return;
_pressed = !digitalRead(_pin);
_lastMs = now;
}
} // namespace drivers

## Slide 9
Led — PWM + Non-blocking Fade
// include/led.h
#pragma once
#include "digital_pin.h"
#include "pwm_pin.h"
namespace drivers {
class Led : public DigitalPin,
public PwmPin {
public:
Led(uint8_t pin, uint8_t channel);
void on();
void off();
void toggle();
void setDutyCycle(uint8_t duty);
void fadeTo(uint8_t target,
uint32_t durationMs);
void update(); // call in loop()
private:
uint8_t _duty;
uint8_t _fadeTarget;
uint32_t _fadeStepMs;
uint32_t _lastFadeMs;
};
} // namespace drivers
Led::Led(uint8_t pin, uint8_t ch)
: DigitalPin(pin, OUTPUT)
, PwmPin(pin, ch)
, _duty(0), _fadeTarget(0)
, _fadeStepMs(0), _lastFadeMs(0) {}
void Led::setDutyCycle(uint8_t d) {
_duty = d;
PwmPin::setDutyCycle(d);
}
void Led::fadeTo(uint8_t t, uint32_t ms) {
_fadeTarget = t;
_fadeStepMs = ms / 256;
_lastFadeMs = millis();
}
void Led::update() {
if (_duty == _fadeTarget) return;
if (millis()-_lastFadeMs < _fadeStepMs)
return;
_duty += (_duty < _fadeTarget) ? 1 : -1;
PwmPin::setDutyCycle(_duty);
_lastFadeMs = millis();
}

## Slide 10
Non-blocking update() Pattern
loop() timeline
0ms
10ms
20ms
30ms
40ms
50ms
60ms
70ms
80ms
btn.isPressed()
led.update()
btn.isPressed()
led.update()
btn.isPressed()
led.update()
update() checks millis()
Returns immediately if not enough time has passed — never blocks
loop() runs at full speed
Other sensors, buttons, Serial all get CPU time every iteration
No delay() in library code
delay() freezes loop() — always forbidden in a reusable driver
_lastFadeMs tracks state
Each Led instance carries its own timer — fully independent

## Slide 11
.h / .cpp Split — Rules
In the header (.h)
#pragma once
class declaration
public / protected / private members
inline functions (if tiny)
NO method bodies
NO #include <Arduino.h>
In the source (.cpp)
#include "own_header.h"
#include <Arduino.h>
Method body implementations
Static member definitions
File-local helpers (anonymous ns)
Remember from Lesson 6: writing Button::onISR() inside the class body in the header
causes IntelliSense error 392 — "member function may not be redeclared outside its class"

## Slide 12
Namespace drivers:: + Include Guards
// Every header:
#pragma once // include guard
namespace drivers {
class Button { ... };
} // namespace drivers
// main.cpp — two options:
// Option A: fully qualified
drivers::Button btn0(0);
drivers::Led red(3, 0);
// Option B: using declaration
using drivers::Button;
using drivers::Led;
Button btn0(0);
Led red(3, 0);
// Option C: using namespace (avoid!)
// using namespace drivers; // pollutes scope
#pragma once vs #ifndef
Both are include guards.
#pragma once is shorter and has no
risk of typos in the guard name.
Why namespace?
Prevents clashes when multiple
libraries define a class called 'Button'.
drivers:: makes the origin explicit.
Option A vs B
Prefer A in headers and large files.
B is fine in main.cpp where the scope
is small and obvious.
Avoid Option C
using namespace in headers leaks
the namespace into every file that
includes yours — pollutes the build.

## Slide 13
Demo — main.cpp
#include <Arduino.h>
#include "button.h"
#include "led.h"
using namespace drivers;
Button btn0(0); // GPIO0, INPUT_PULLUP
Button btn1(1); // GPIO1
Led red(3, 0); // GPIO3, LEDC ch0
Led grn(10,1); // GPIO10, LEDC ch1
void IRAM_ATTR isr0() { btn0.onISR(); }
void IRAM_ATTR isr1() { btn1.onISR(); }
void setup() {
attachInterrupt(0, isr0, CHANGE);
attachInterrupt(1, isr1, CHANGE);
}
void loop() {
if (btn0.isPressed())
red.fadeTo(255, 1000);
else
red.fadeTo(0, 1000);
if (btn1.isPressed()) grn.toggle();
red.update();
}
BTN0 (GPIO0)
Hold → red LED fades in (1 s)
Release → fades out (1 s)
BTN1 (GPIO1)
Press → green LED toggles on/off
(single ISR edge)
red.update()
Called every loop() iteration
Moves fade by 1 step if timer elapsed
Global objects
Constructed before setup()
Constructors run pinMode + ledcSetup

## Slide 14
Common Pitfalls
Missing virtual destructor in base class
// bad: class DigitalPin { ~DigitalPin() {} };
// good: class DigitalPin { virtual ~DigitalPin() {} };
Without virtual, deleting a derived object through a base pointer skips the derived destructor — resource leak.
Copying a pin object
// bad: Button b2 = btn0; // copies _pin value
// good: Button(const Button&) = delete;
Two objects owning the same GPIO pin cause double-attach / double-detach bugs. Disable copy.
Reading _pressed without volatile
// bad: bool _pressed; // may be cached in register
// good: volatile bool _pressed; // always re-read
ISR and loop() run in different contexts. Without volatile the compiler may not see the ISR update.

## Slide 15
Homework — Implement the Library
You receive (scaffolding)
Complete .h files (declarations)
button.cpp with TODO stubs
led.cpp with TODO stubs
Finished main.cpp (do not edit)
platformio.ini configured
Your task
Button::Button() constructor
Button::isPressed()
Button::onISR() with debounce
Led::Led() constructor
Led::on() / off() / toggle()
Led::setDutyCycle()
Led::fadeTo() + Led::update()
Expected result:
BTN0 held → red LED fades in (1 s) | BTN0 released → red fades out | BTN1 press → green toggles

## Slide 16
Lesson 9 — Summary
GPIO abstraction
DigitalPin, AnalogPin, PwmPin hide low-level calls behind a clean interface
Inheritance
Button and Led extend DigitalPin — reuse without duplication
RAII in drivers
Constructors call pinMode / ledcSetup; destructors clean up automatically
Non-blocking update()
millis() state machine — never delay() in a reusable driver
Library discipline
#pragma once, namespace drivers::, .h/.cpp split, no Arduino.h in headers
Pitfalls
virtual destructor, delete copy ctor, volatile for ISR-shared variables
Next: Lesson 10