## Slide 1
Lesson 5
Interrupts, Timers & PWM
From Polling to Event-Driven Embedded Programming
Interrupts
Timers
PWM
Embedded C/C++ Development | ESP32-C3

## Slide 2
enum: Named Constants
Why Use enum?
Replace magic numbers with names
Compiler checks value correctness
Self-documenting code
Groups related constants together
typedef enum { LED_OFF = 0, LED_RED = 1, LED_GREEN = 2, LED_BLUE = 3 } led_color_t;
BAD: Magic Numbers
if (state == 3) { // what is 3?
set_color(2);
// ???
}
GOOD: Named Constants
if (state == LED_BLUE) { set_color(LED_GREEN); }

## Slide 3
enum in Embedded Systems
State Machine Pattern
typedef enum {
STATE_IDLE,
STATE_RUNNING,
STATE_ERROR,
STATE_COUNT // total states
} state_t;
state_t current = STATE_IDLE;
switch (current) {
case STATE_IDLE: break;
case STATE_RUNNING: break;
case STATE_ERROR: break;
}
Key Tips
Values start at 0 by default
Use _COUNT as last entry for array sizing
Prefix names: STATE_, LED_, MODE_
Use typedef for cleaner declarations
Under the Hood
// enum is just an int!
sizeof(state_t) // usually 4 bytes
// For memory-constrained code:
typedef uint8_t led_color_t;
#define LED_OFF 0
#define LED_RED 1
Now that we can name our states cleanly, let's learn how to REACT to events...

## Slide 4
Part 1
Hardware Interrupts
Stop Wasting CPU Cycles

## Slide 5
Polling vs. Interrupts
Polling (what you did before)
void loop() {
// CPU checks EVERY cycle
if (digitalRead(BTN) == LOW) {
handle_press();
}
// ... other work blocked
}
- CPU busy-waits constantly
- Wastes power
- Can miss fast events
- Blocks other tasks
Interrupts (event-driven)
void IRAM_ATTR onPress() {
// runs ONLY when pressed
flag = true;
}
// CPU free for other work!
attachInterrupt(BTN, onPress,
FALLING);
+ CPU does useful work
+ Low power consumption
+ Instant response
+ Non-blocking design
Think of it: a doorbell vs. checking the door every 5 seconds

## Slide 6
How Interrupts Work
1
CPU executes
main code
2
Event occurs
(button press)
3
CPU saves state
& jumps to ISR
4
ISR runs
(keep it SHORT!)
5
CPU restores
& resumes main
Trigger Modes
RISING
LOW -> HIGH
_/^^
FALLING
HIGH -> LOW
^^\_
CHANGE
Any transition
_/^^\_
LOW / HIGH
Level trigger
___ ^^^

## Slide 7
ISR Rules (Critical!)
Keep It Short
ISR should set a flag and exit.
Do heavy work in loop().
Use volatile
Variables shared with ISR
must be declared volatile.
No Serial / delay
No Serial.print(), no delay(),
no malloc() inside ISR.
IRAM_ATTR
ESP32 ISRs must be in IRAM.
Add IRAM_ATTR to function.
volatile bool buttonPressed = false; // shared with ISR -> volatile!
void IRAM_ATTR handleButton() { buttonPressed = true; } // short! just set flag
void loop() { if (buttonPressed) { buttonPressed = false; /* do work here */ } }

## Slide 8
Part 2
Hardware Timers
Precise Timing Without delay()

## Slide 9
What Are Hardware Timers?
Hardware Counter
A timer is a counter driven by a clock
It counts up (or down) at a fixed frequency
When it reaches a target value, it can:
- Trigger an interrupt
- Toggle a GPIO pin (PWM!)
- Reset and start over
delay(1000)
Blocks CPU for 1 second.
Nothing else can run!
Hardware Timer
Counts in background.
CPU is free! Fires interrupt
when time is up.
ESP32-C3 Timer Resources
Resource | Count | Resolution | Used For
General Purpose Timers | 2 | 54-bit | Periodic tasks, timing
LEDC PWM channels | 6 | Up to 14-bit | LED/motor control

## Slide 10
Part 3
PWM & LEDC
Analog Output from Digital Pins

## Slide 11
What Is PWM?
Pulse Width Modulation: rapidly switching a pin ON/OFF to simulate an analog voltage
0%
Always OFF
LED off
25%
ON 1/4 of time
Dim
50%
ON half of time
Medium
75%
ON 3/4 of time
Bright
100%
Always ON
Full
Key parameters: Frequency (Hz) controls flicker, Resolution (bits) controls precision

## Slide 12
ESP32 LEDC API (Arduino)
ESP32 Arduino Core 3.x (new API)
// Step 1: Attach pin with frequency and resolution
ledcAttach(pin, frequency, resolution_bits);
// pin: GPIO number
// frequency: PWM frequency in Hz (e.g. 5000)
// resolution: bit depth (1-14 on ESP32-C3)
// Step 2: Set duty cycle
ledcWrite(pin, duty);
// duty: 0 to (2^resolution - 1)
// 8-bit: 0..255 10-bit: 0..1023
// 12-bit: 0..4095 14-bit: 0..16383
// Step 3: (optional) Detach when done
ledcDetach(pin);
Resolution vs. Duty Range
Bits | Max Duty | Steps | Good For
8 | 255 | 256 | Simple LED control
10 | 1023 | 1024 | Servo, motors
12 | 4095 | 4096 | Smooth fading
Frequency vs Resolution
Higher resolution = lower max
frequency. For LEDs, 5 kHz
at 8-bit (or 10-bit) is perfect.
max_freq = 80MHz / 2^bits

## Slide 13
RGB Color Mixing with PWM
#define PIN_R 3
#define PIN_G 4
#define PIN_B 5
#define PWM_FREQ 5000
#define PWM_RES 8 // 0..255
void setup() {
ledcAttach(PIN_R, PWM_FREQ, PWM_RES);
ledcAttach(PIN_G, PWM_FREQ, PWM_RES);
ledcAttach(PIN_B, PWM_FREQ, PWM_RES);
}
void setColor(uint8_t r, uint8_t g,
uint8_t b) {
ledcWrite(PIN_R, r);
ledcWrite(PIN_G, g);
ledcWrite(PIN_B, b);
}
Color Examples
Red
(255, 0, 0)
Green
(0, 255, 0)
Blue
(0, 0, 255)
Yellow
(255, 255, 0)
Cyan
(0, 255, 255)
Magenta
(255, 0, 255)
White
(255, 255, 255)
Orange
(255, 128, 0)
Note: Common Anode RGB LED? Invert values: ledcWrite(pin, 255 - value). Common Cathode? Use values directly. Check your LED datasheet!

## Slide 14
Putting It All Together
Interrupt + enum + PWM = Smart RGB Controller
Button Press
(hardware event)
ISR
(set flag)
loop()
(read flag,
next enum state)
PWM Output
(RGB LED)
->
->
->
typedef enum { COLOR_RED, COLOR_GREEN, COLOR_BLUE, COLOR_YELLOW,
COLOR_CYAN, COLOR_MAGENTA, COLOR_WHITE, COLOR_COUNT } color_t;
volatile bool btnPressed = false;
color_t currentColor = COLOR_RED;
void IRAM_ATTR onButton() { btnPressed = true; }
void setup() {
attachInterrupt(BTN_PIN, onButton, FALLING);
ledcAttach(PIN_R, 5000, 8); ledcAttach(PIN_G, 5000, 8); ledcAttach(PIN_B, 5000, 8);
}
void loop() {
if (btnPressed) {
btnPressed = false;
currentColor = (color_t)((currentColor + 1) % COLOR_COUNT);
applyColor(currentColor); // sets R, G, B via ledcWrite()
} }

## Slide 15
Homework: RGB PWM Controller
Requirements
1. Use enum for color states
2. Button via interrupt (not polling!)
3. PWM output to RGB LED (3 channels)
4. At least 6 distinct colors
5. Debounce the interrupt
6. Serial output: print color name
Bonus Challenge
Smooth fade between colors
Second button: brightness control
Auto-cycle mode (timer-based)
Hints
Use millis() for debounce timing
Store colors in a struct array
Use COLOR_COUNT for modulo wrap
Due: before next lesson | Push to your GitHub repo

## Slide 16
Questions?
Today: enum + Interrupts + Timers + PWM / LEDC
Next lesson: I2C Communication & Sensors