## Slide 1
Lesson 19
REST APIs and JSON
on ESP32
Fetching live electricity prices from the Elering Dashboard API
Fundamentals of C++ for Microcontrollers | Module 4

## Slide 2
Lesson Goals
HTTP GET
Make requests to public REST APIs
using the HTTPClient library
ArduinoJson
Parse JSON responses and extract
typed data fields safely
NTP Sync
Synchronize the ESP32 real-time clock
over the network
WS2812
Map the current electricity price to
an RGB color (green = cheap, red = expensive)

## Slide 3
The Big Picture
ESP32
lolin_c3_mini
WiFi
WPA2 / DHCP
HTTPS GET
HTTPClient
JSON Parse
ArduinoJson
Output
Serial + WS2812
start=2026-04-17T00:00:00Z & end=2026-04-17T23:59:59Z
Response JSON:
{
"success": true,
"data": {
"ee": [
{ "timestamp": 1745535600, "price": 85.23 },
{ "timestamp": 1745539200, "price": 79.10 }
],
"fi": [ ... ], "lv": [ ... ], "lt": [ ... ]
}
}

## Slide 4
The Elering Dashboard API
Endpoint
GET /api/nps/price
Base URL
https://dashboard.elering.ee
Query parameters
start - begin datetime (ISO 8601)
end - end datetime (ISO 8601)
Maximum range: 1 year per request
Price unit
EUR / MWh (divide by 1000 for EUR/kWh)
Countries in response
ee fi lv lt
{
"success": true,
"data": {
"ee": [
{
"timestamp": 1745535600,
"price": 85.23
},
{
"timestamp": 1745539200,
"price": 79.10
}
],
"fi": [ ... ],
"lv": [ ... ],
"lt": [ ... ]
}
}

## Slide 5
WiFi Connection Recap
WiFi.begin(ssid, pass)
Initiates the connection attempt. Non-blocking: call repeatedly or poll with WiFi.status().
WL_CONNECTED
The status constant that means the connection is established.
WiFi.localIP()
Returns the IP address assigned by the DHCP server.
Keep credentials in config.h
Never commit SSID / password
to a public repository.
#include <WiFi.h>
#include "config.h" // SSID, PASSWORD
void connectWiFi() {
WiFi.begin(SSID, PASSWORD);
Serial.print("Connecting");
while (WiFi.status() != WL_CONNECTED) {
delay(500);
Serial.print(".");
}
Serial.println();
Serial.print("IP: ");
Serial.println(WiFi.localIP());
}

## Slide 6
HTTPClient: Making the GET Request
WiFiClientSecure
Wraps a TLS socket. Call setInsecure() to skip certificate validation (demo only).
http.begin(client, url)
Pass the secure client and the full URL string.
http.GET()
Returns the HTTP status code. 200 = OK, negative = error.
http.getString()
Returns the full response body.
Call after a successful GET().
#include <WiFiClientSecure.h>
#include <HTTPClient.h>
String fetchPrices(const String& url) {
WiFiClientSecure client;
// skip TLS cert check (demo only)
client.setInsecure();
HTTPClient http;
http.begin(client, url);
int code = http.GET();
if (code == HTTP_CODE_OK) {
String body = http.getString();
http.end();
return body;
}
Serial.printf("HTTP error: %d\n", code);
http.end();
return "";
}

## Slide 7
JSON Basics
JSON (JavaScript Object Notation) is a text-based data format.
Every REST API response you will encounter uses JSON.
{
"success": true, // bool
"count": 24, // number (integer)
"version": "1.3.0", // string
"data": { // nested object
"ee": [ // array
{
"timestamp": 1745535600,
"price": 85.23 // number (float)
}
]
}
}
JSON types
string
"hello"
number
42 or 3.14
boolean
true / false
null
null
array
[ ... ]
object
{ ... }

## Slide 8
ArduinoJson: Parsing the Response
Install (platformio.ini):
bblanchon/ArduinoJson @ ^7.0.0
JsonDocument
One type for both objects and arrays. Heap-allocated.
deserializeJson(doc, src)
Parses the JSON string. Returns DeserializationError.
doc["key"].as<T>()
Returns a typed value.
Use [] for both keys and indices.
#include <ArduinoJson.h>
void parseResponse(const String& body) {
JsonDocument doc;
DeserializationError err =
deserializeJson(doc, body);
if (err) {
Serial.print("Parse error: ");
Serial.println(err.c_str());
return;
}
if (!doc["success"].as<bool>()) return;
// Navigate nested objects
JsonArray ee =
doc["data"]["ee"].as<JsonArray>();
Serial.printf("Entries: %u\n",
ee.size());
}

## Slide 9
Parsing the Price Array
PriceEntry struct
Holds one hourly record: timestamp (Unix UTC) and price in EUR/MWh.
Range-for over JsonArray
ArduinoJson supports modern C++ range-for directly.
.as<uint32_t>()
Explicit cast from JsonVariant to a fixed-width type.
MAX_ENTRIES = 25
24 hours + 1 spare.
Protects against buffer overrun.
struct PriceEntry {
uint32_t timestamp; // Unix UTC
float price; // EUR/MWh
};
static const uint8_t MAX_ENTRIES = 25u;
uint8_t parsePriceArray(
JsonArray arr,
PriceEntry* out) {
uint8_t count = 0u;
for (JsonObject obj : arr) {
if (count >= MAX_ENTRIES) break;
out[count].timestamp =
obj["timestamp"].as<uint32_t>();
out[count].price =
obj["price"].as<float>();
count++;
}
return count;
}

## Slide 10
Finding Min, Max, and Current Hour
Algorithm
Single pass through the array. Track min, max, and match the current hour.
Hour matching
Floor current time to nearest hour:
h0 = (now / 3600) * 3600
curPrice = -1.0f
Sentinel value: the current hour
may not be in the array yet.
struct PriceSummary {
float minPrice;
float maxPrice;
float curPrice; // -1 if not found
uint8_t minHour;
uint8_t maxHour;
};
PriceSummary analyze( const PriceEntry* e,
uint8_t n, time_t now) {
PriceSummary r = { e[0].price, e[0].price,
-1.0f, 0u, 0u };
time_t h0 = (now / 3600) * 3600;
for (uint8_t i = 0u; i < n; i++) {
if (e[i].price < r.minPrice)
{ r.minPrice = e[i].price; r.minHour = i; }
if (e[i].price > r.maxPrice)
{ r.maxPrice = e[i].price; r.maxHour = i; }
if ((time_t)e[i].timestamp == h0)
r.curPrice = e[i].price;
}
return r;
}

## Slide 11
NTP Time Synchronization
NTP
Network Time Protocol. configTime() enables SNTP on the ESP32.
configTime(tz, dst, server)
tz = UTC offset in seconds dst = daylight saving offset
Estonia (EET / UTC+2)
7200 seconds offset. DST = 0 for simplicity.
time(&t)
Returns the current Unix UTC
timestamp in seconds.
Use this to match API timestamps.
#include <time.h>
static const long TZ_OFFSET = 7200L;
static const int DST_OFFSET = 0;
void syncNTP() {
configTime(TZ_OFFSET, DST_OFFSET, "pool.ntp.org",
"time.nist.gov");
struct tm ti;
Serial.print("NTP sync");
while (!getLocalTime(&ti)) {
delay(500);
Serial.print(".");
}
Serial.printf( "\nTime: %02d:%02d:%02d\n",
ti.tm_hour, ti.tm_min, ti.tm_sec);
}
time_t nowUnix() {
time_t t;
time(&t);
return t;
}

## Slide 12
WS2812 Color Feedback
Idea
Map the current price between today's min and max onto a green-to-red gradient.
ratio = 0.0 -> green (cheap)
ratio = 1.0 -> red (expensive)
constrain()
Clamps ratio to [0, 1] to guard against out-of-range values.
GPIO 8
Onboard WS2812 on the
ESP32-C3 Super Mini.
#include <Adafruit_NeoPixel.h>
#define LED_PIN 8
#define LED_CNT 1
#define MAX_BR 80u // brightness cap
Adafruit_NeoPixel strip(
LED_CNT, LED_PIN,
NEO_GRB + NEO_KHZ800);
void initLed() {
strip.begin();
strip.show();
}
void showPrice(float cur,
float lo, float hi) {
float ratio = (cur - lo) / (hi - lo);
ratio = constrain(ratio, 0.0f, 1.0f);
uint8_t R = (uint8_t)(ratio * MAX_BR);
uint8_t G = (uint8_t)(
(1.0f - ratio) * MAX_BR);
strip.setPixelColor(
0, strip.Color(R, G, 0u));
strip.show();
}

## Slide 13
Demo Code Structure
platformio.ini
ESP32-C3 board, ArduinoJson + Adafruit NeoPixel libs
include/config.h
SSID, PASSWORD, constants (do not commit to git)
include/wifi_helper.h
connectWiFi() declaration
src/wifi_helper.cpp
WiFi.begin() + status polling, NTP sync
include/elering.h
PriceEntry, PriceSummary structs + function declarations
src/elering.cpp
buildUrl(), fetchPrices(), parsePriceArray(), analyze()
include/led.h
initLed(), showPrice() declarations
src/led.cpp
Adafruit NeoPixel color mapping (green to red)
src/main.cpp
setup(): WiFi -> NTP -> fetch -> parse -> LED loop(): timed refresh

## Slide 14
Homework
Extend the demo project with the following features:
1
Top-3 cheapest hours
Find the three cheapest hours of today. Print each one as HH:00 with its price in EUR/MWh. (Hint: sort or scan three times.)
2
Price category display
Define: cheap (<50), normal (50-100), expensive (>100) EUR/MWh. Print the category to Serial each refresh cycle.
3
Periodic refresh with millis()
Fetch new prices once per hour without blocking. Use millis() to track elapsed time. Do not use delay() for long waits.