## Slide 1
Lesson 15
RP2350: Meet the New Platform
Fundamentals of C++ for Microcontrollers | Module 4
Dual-Core ARM Cortex-M33 / RISC-V Hazard3 | Pico SDK | PlatformIO

## Slide 2
Lesson 15 | RP2350: Meet the New Platform
2
Module 4: Platform Roadmap
ESP32-C3
Lessons 10-11
COMPLETED
STM32
Lessons 12-14
COMPLETED
RP2350
Lesson 15+
CURRENT
Cross-Platform Comparison coming after all three platforms are covered

## Slide 3
Lesson 15 | RP2350: Meet the New Platform
3
RP2350 at a Glance
CORES
2x Cortex-M33
or 2x Hazard3
CLOCK
150 MHz
SRAM
520 KB
FLASH
External QSPI
(board: 4-16MB)
GPIO (A)
30 pins
PIO
3 blocks
12 state machines
ADC
12-bit, 4 ch
(8 ch on B)
SECURITY
ARM TrustZone
Signed Boot

## Slide 4
Lesson 15 | RP2350: Meet the New Platform
4
RP2040 vs RP2350
Feature | RP2040 | RP2350
CPU | 2x Cortex-M0+ | 2x Cortex-M33 / Hazard3
Clock | 133 MHz | 150 MHz
SRAM | 264 KB | 520 KB
PIO Blocks | 2 (8 SM) | 3 (12 SM)
ADC | 12-bit, 4 ch | 12-bit, 4/8 ch
FP Unit | None | Single + Double
Security | None | TrustZone + OTP
USB | 1.1 Host/Device | 1.1 Host/Device
HSTX | No | Yes (DVI out)

## Slide 5
Lesson 15 | RP2350: Meet the New Platform
5
Dual Architecture: ARM + RISC-V
ARM Cortex-M33
ARMv8-M architecture
DSP instructions
Single + Double FPU
TrustZone security
Default mode at boot
RISC-V Hazard3
RV32IMAC instruction set
Open-source core design
No FPU (software float)
No TrustZone
Selectable at boot time
Only 2 cores active at a time. You can even run one ARM + one RISC-V core simultaneously.

## Slide 6
Lesson 15 | RP2350: Meet the New Platform
6
Our Board: RP2350 USB Dongle
RP2350A USB-A Form Factor
Chip: RP2350A (QFN-60, 30 GPIO)
Flash: 4-16 MB QSPI (board-dependent)
SRAM: 520 KB on-chip
USB-A male connector (plug-and-play)
BOOT + RST buttons on board
~15 GPIO exposed via castellated pads
No onboard LED
Key Differences
vs Pico 2
USB-A (no cable needed)
Smaller footprint
Fewer exposed GPIOs
No onboard LED
Same RP2350A chip

## Slide 7
Lesson 15 | RP2350: Meet the New Platform
7
Toolchain: PlatformIO + Pico SDK
Setup Steps
1
Install PlatformIO in VS Code (if not already done)
2
Create new project: Board = rpipico2
3
Set platform to maxgerhardt's fork (RP2350 support)
4
Set framework = arduino (wraps Pico SDK)
5
Enable Win32 Long Paths (Windows only)
6
Build -> generates .uf2 firmware file
Fallback: Official Raspberry Pi Pico VS Code Extension (CMake + Pico SDK native)

## Slide 8
Lesson 15 | RP2350: Meet the New Platform
8
platformio.ini
[env:rp2350_usb]
platform = https://github.com/maxgerhardt/
platform-raspberrypi.git
board = rpipico2
framework = arduino
board_build.core = earlephilhower
; RP2350 defaults to ARM Cortex-M33
; For RISC-V, uncomment:
; board_build.mcu = rp2350-riscv
monitor_speed = 115200
We use Arduino framework as a wrapper -- Pico SDK APIs are fully accessible underneath

## Slide 9
Lesson 15 | RP2350: Meet the New Platform
9
Blink Demo: External LED Wiring
No onboard LED -- wire an external one
Circuit
GP15 --> 330 Ohm --> LED (anode) --> GND
LED forward voltage: ~2V (red)
Current: (3.3V - 2V) / 330 = ~4 mA
Pin Details
GPIO 15 chosen because:
Available on most dongles
No special function
Not used by QSPI flash
3.3V logic level output

## Slide 10
Lesson 15 | RP2350: Meet the New Platform
10
Blink: Pico SDK Style Code
#include "pico/stdlib.h"
const uint LED_PIN = 15;
int main() {
stdio_init_all();
gpio_init(LED_PIN);
gpio_set_dir(LED_PIN, GPIO_OUT);
while (true) {
gpio_put(LED_PIN, 1);
sleep_ms(500);
gpio_put(LED_PIN, 0);
sleep_ms(500);
}
}
Key Functions
stdio_init_all()
Init USB/UART serial
gpio_init()
Enable GPIO pad
gpio_set_dir()
Set pin direction
gpio_put()
Set pin high/low
sleep_ms()
Blocking delay

## Slide 11
Lesson 15 | RP2350: Meet the New Platform
11
Build & Flash: UF2 Workflow
1
Build in PlatformIO
Click Build (checkmark icon) or Ctrl+Alt+B.
Output: .pio/build/rp2350_usb/firmware.uf2
2
Enter BOOTSEL Mode
Hold BOOT button, plug USB dongle into PC.
Board appears as mass storage device (RPI-RP2).
3
Flash Firmware
Drag-and-drop firmware.uf2 onto the RPI-RP2 drive.
Board reboots automatically and runs your code.
4
Monitor Serial Output
Open PlatformIO Serial Monitor (115200 baud).
USB CDC serial -- no extra UART wiring needed.

## Slide 12
Homework & Next Steps
Homework
Set up PlatformIO project for RP2350 USB
Wire external LED on GPIO 15
Flash blink demo via BOOTSEL + UF2
Modify: add a second LED, alternate blink
Explore: try printf() over USB serial
Coming Up
GPIO: buttons + interrupts on RP2350
UART & I2C peripherals
PIO state machines (unique to RP2xxx)
Cross-platform comparison: ESP32 vs STM32 vs RP2350
Push your project to GitHub Classroom before next session