## Slide 1
Lesson 16
WS2812 Addressable LEDs
Fundamentals of C++ for Microcontrollers | Module 4
Protocol | Bit-Banging Driver | 10-LED Ring | RP2350 USB

## Slide 2
Lesson 16 | WS2812 Addressable LEDs
2
What Are Addressable LEDs?
Regular LED
One GPIO per LED
Only ON or OFF (or PWM)
Fixed color
10 LEDs = 10 GPIOs
No individual brightness control
WS2812 (NeoPixel)
One GPIO for ANY number of LEDs
Each LED has a built-in controller
Full RGB (24-bit color per LED)
10 LEDs = 1 GPIO
Daisy-chained (data cascades)

## Slide 3
Lesson 16 | WS2812 Addressable LEDs
3
Inside a WS2812 LED
4 Pins
VDD
Power (5V)
GND
Ground
DIN
Data In
DOUT
Data Out (to next LED)
Built-in Controller
Each LED contains:
Shift register (24-bit)
Constant-current driver
3 PWM channels (R, G, B)
Signal reshaping logic
Consumes first 24 bits,
passes the rest to DOUT

## Slide 4
Lesson 16 | WS2812 Addressable LEDs
4
Data Format: GRB, 24 Bits per LED
G7 G6 G5 G4 G3 G2 G1 G0
GREEN (byte 0)
R7 R6 R5 R4 R3 R2 R1 R0
RED (byte 1)
B7 B6 B5 B4 B3 B2 B1 B0
BLUE (byte 2)
MSB first -->
Color order is GRB, not RGB!
Each bit is sent MSB first (bit 7 -> bit 0)
24 bits total per LED: 8 green + 8 red + 8 blue
For N LEDs, send N x 24 bits continuously
End with a reset pulse (>50 us LOW) to latch data

## Slide 5
Lesson 16 | WS2812 Addressable LEDs
5
Protocol Timing
Bit "0"
HIGH
LOW
T0H = 400 ns
T0L = 850 ns
Bit "1"
HIGH
LOW
T1H = 800 ns
T1L = 450 ns
The bit value is encoded by the duty cycle: long HIGH = 1, short HIGH = 0
Reset: Hold LOW for >50 us (>280 us recommended) to latch all data into LEDs

## Slide 6
Lesson 16 | WS2812 Addressable LEDs
6
Cascading: Data Flows Through the Chain
MCU
GP22
LED 0
LED 1
LED 2
...
LED 9
DIN DOUT DIN DOUT DIN DOUT
How the cascade works:
MCU sends 10 x 24 = 240 bits (for 10 LEDs)
LED 0 grabs the first 24 bits, passes the rest to DOUT
LED 1 grabs the next 24 bits, passes the rest...
After all bits sent, MCU sends RESET (>50 us LOW)
All LEDs update simultaneously on RESET!

## Slide 7
Lesson 16 | WS2812 Addressable LEDs
7
Our Board: TENSTAR RP2350-USB
Board Features
RP2350A, dual Cortex-M33 @ 150 MHz
16 MB QSPI Flash (W25Q128)
520 KB SRAM
USB-A male connector
BOOT + RST buttons
Onboard WS2812 RGB LED on GP22
Today's Plan
1
Test onboard WS2812 on GP22
2
Write a bit-bang WS2812 driver
3
Connect 10-LED ring on GP15
4
Run rainbow animation

## Slide 8
Lesson 16 | WS2812 Addressable LEDs
8
Bit-Banging: Generating the Signal
void sendBit(uint pin, bool bit) {
if (bit) { // Send '1'
gpio_put(pin, 1);
busy_wait_ns(800); // T1H = 800 ns
gpio_put(pin, 0);
busy_wait_ns(450); // T1L = 450 ns
} else { // Send '0'
gpio_put(pin, 1);
busy_wait_ns(400); // T0H = 400 ns
gpio_put(pin, 0);
busy_wait_ns(850); // T0L = 850 ns
}
}
Interrupts disabled during transmission to protect timing-critical signal

## Slide 9
Lesson 16 | WS2812 Addressable LEDs
9
Driver: sendByte & sendPixel
void sendByte(uint pin, uint8_t byte) {
for (int i = 7; i >= 0; i--) { // MSB first
sendBit(pin, byte & (1 << i));
}
}
void sendPixel(uint pin,
uint8_t r, uint8_t g, uint8_t b) {
sendByte(pin, g); // GRB order!
sendByte(pin, r);
sendByte(pin, b);
}
void sendReset(uint pin) {
gpio_put(pin, 0);
sleep_us(300); // >50 us reset pulse
}

## Slide 10
Lesson 16 | WS2812 Addressable LEDs
10
Wiring the 10-LED Ring
Connections
Ring VDD
-->
5V (VBUS pin)
Ring GND
-->
GND
Ring DIN
-->
GP15
Important Notes
Power from USB: 10 LEDs at 20mA each = 200mA max (OK for USB)
Signal is 3.3V, WS2812 spec says 5V logic, but 3.3V works reliably for short runs
Add 300-500 Ohm resistor on data line (optional but recommended)
Keep wires short to reduce noise
GP22 = onboard WS2812 (1 LED, soldered) GP15 = external ring (10 LEDs, wired)

## Slide 11
Lesson 16 | WS2812 Addressable LEDs
11
Power & Signal Considerations
Power Budget
Each WS2812 draws up to:
~20 mA per channel at full brightness
~60 mA per LED (full white)
~1 mA idle (controller only)
10 LEDs full white = 600 mA
USB 2.0 port provides 500 mA
Limit brightness in code to stay safe!
3.3V vs 5V Logic
WS2812 spec: VIH = 0.7 x VDD
At VDD=5V: VIH = 3.5V
RP2350 outputs 3.3V
Technically out of spec!
In practice: works fine for
short runs (<1m) and small LED counts.
For production: use a level shifter
(74AHCT125 or similar).

## Slide 12
Homework & Next Steps
Homework
Implement 3 LED ring effects:
Chase: single lit LED moves around ring
Breathing: all LEDs fade in/out smoothly
Color wipe: ring fills one LED at a time
Use a button to cycle between effects
Coming Up
PIO state machines: hardware WS2812 driver
Why PIO is better than bit-banging
I2C / SPI on RP2350
Cross-platform comparison
Push your project to GitHub Classroom before next session