## Slide 1
Lesson 12
STM32 Ecosystem
and GPIO
CubeMX + CubeIDE | HAL | Nucleo-F3334R8
Module 4
STM32
HAL
Fundamentals of C++ for Microcontrollers | 2026

## Slide 2
Lesson 12 — Agenda
What we cover today
1
STM32 Family Overview
Product lines F0/F1/F4/H7, naming convention, where F334 fits
2
Development Ecosystem
CubeMX, CubeIDE, HAL vs LL vs CMSIS, ST-Link debugger
3
CubeMX Walkthrough
Pinout editor, clock tree configuration, code generation
4
Generated Project Structure
.ioc file, Core/, Drivers/, USER CODE sections
5
Nucleo-F334R Board Overview
Morpho connectors, LD2 = PA5, B1 = PC13, ST-Link on-board
6
HAL GPIO API
HAL_GPIO_WritePin, ReadPin, TogglePin, Init struct
7
Demo
Blink LD2, read B1 — first HAL project on Nucleo
Fundamentals of C++ for Microcontrollers | Module 4 | Lesson 12 | 2026

## Slide 3
STM32 Family Overview
Cortex-M based MCUs from STMicroelectronics
STM32F0 / F1
Cortex-M0/M3
Up to 72 MHz
Entry-level, low cost
STM32F4
Cortex-M4F
Up to 180 MHz
Mainstream + FPU
STM32H7
Cortex-M7
Up to 480 MHz
High performance
STM32L4 / U5
Cortex-M4/M33
Up to 120 MHz
Ultra-low power
Naming convention:
STM32 F 3 3 4 R 8
Family
Product line
(F=mainstream
L=low-power)
Subline
(3=Cortex-M4)
Part number
Pin count
(R=64 pins)
Flash size
(64KB)
Our board
Fundamentals of C++ for Microcontrollers | Module 4 | Lesson 12 | 2026
Link to bard description https://os.mbed.com/platforms/ST-Nucleo-F334R8/

## Slide 4
STM32 Development Ecosystem
Tools that work together
STM32CubeMX
Graphical pinout editor
Clock tree configurator
Peripheral setup wizard
Generates C project skeleton
.ioc project file
STM32CubeIDE
Eclipse/CDT based IDE
CubeMX built-in
ARM GCC toolchain
ST-Link debug (SWD)
SWV live data viewer
HAL / LL / CMSIS
HAL: high-level, portable
LL: low-level, fast
CMSIS: Cortex-M standard
HAL = what we use
LL for performance-critical
ST-Link: on-board debugger/programmer on Nucleo — connects via USB, programs and debugs over SWD (2-wire)
Fundamentals of C++ for Microcontrollers | Module 4 | Lesson 12 | 2026

## Slide 5
CubeMX — Pinout & Peripherals
Step 1 of 3: configure what pins do
1
New Project
File > New Project > Board Selector > NUCLEO-F334
2
Pinout View
Each pin shown on chip diagram — click to assign function
3
Assign GPIO
PA5: GPIO_Output (LD2), PC13: GPIO_Input (B1 button)
4
Label pins
Right-click pin > Enter User Label for readable names
Nucleo-F334 Key Pins
PA5
GPIO_Output
LD2 (green LED)
PC13
GPIO_Input
B1 (blue button)
PA2
USART2_TX
ST-Link UART TX
PA3
USART2_RX
ST-Link UART RX
PA13
SYS_JTMS
ST-Link SWD (SWDIO)
PA14
SYS_JTCK
ST-Link SWD (SWCLK)
Fundamentals of C++ for Microcontrollers | Module 4 | Lesson 12 | 2026

## Slide 6
CubeMX Walkthrough — Clock Tree
Step 2 of 3: configure system clocks
HSE
8 MHz
(Nucleo crystal)
PLL
x84 / 2
SYSCLK
84 MHz
AHB
84 MHz
(/ 1)
APB2
84 MHz
(/ 1)
APB1
42 MHz
(/ 2)
Key points:
Nucleo-F401RE runs at 84 MHz (not 168 MHz max — HSE 8 MHz limits PLL on this board)
APB1 max = 42 MHz — affects UART/I2C/SPI baud rate calculations
CubeMX shows clock errors in red if you exceed limits
HAL_RCC_GetSysClockFreq() returns SYSCLK at runtime
Fundamentals of C++ for Microcontrollers | Module 4 | Lesson 12 | 2026

## Slide 7
CubeMX Walkthrough — Code Generation
Step 3 of 3: generate the project
Project Manager tab
Set project name, location, toolchain = STM32CubeIDE
Code Generator tab
Copy only necessary library files (not full HAL)
Generate Code
Button top-right — creates full project with Makefile
Open in CubeIDE
IDE opens automatically, ready to build and flash
main.c — USER CODE sections
/* USER CODE BEGIN Includes */
#include "my_driver.h"
/* USER CODE END Includes */
int main(void) {
HAL_Init();
SystemClock_Config();
MX_GPIO_Init();
/* USER CODE BEGIN 2 */
my_init();
/* USER CODE END 2 */
while (1) {
/* USER CODE BEGIN 3 */
my_loop();
/* USER CODE END 3 */
}
}
CubeMX will NOT overwrite USER CODE sections on regeneration
Fundamentals of C++ for Microcontrollers | Module 4 | Lesson 12 | 2026

## Slide 8
Generated Project Structure
What CubeMX creates inside CubeIDE
MyProject/
MyProject.ioc
Core/
Inc/
main.h
stm32f4xx_hal_conf.h
Src/
main.c
stm32f4xx_hal_msp.c
stm32f4xx_it.c
system_stm32f4xx.c
Drivers/
STM32F4xx_HAL_Driver/
CMSIS/
startup_stm32f401retx.s
.ioc file
CubeMX project — source of truth for peripheral config. Re-open to change settings and regenerate.
main.c
Your application entry point. Contains USER CODE sections — safe to edit.
HAL_Driver/
ST-provided HAL source. Never edit — will be overwritten on regeneration.
*_it.c
Interrupt handlers. CubeMX generates stubs; add your ISR code in USER CODE sections.
startup_*.s
Assembler startup file. Sets up stack, calls SystemInit(), then jumps to main().
Fundamentals of C++ for Microcontrollers | Module 4 | Lesson 12 | 2026

## Slide 9
Nucleo-F401RE Board Overview
Know your hardware before writing code
MCU
STM32F401RET6 — Cortex-M4 @ 84 MHz, 512KB Flash, 96KB SRAM
Debugger
ST-Link v2-1 on-board — no external programmer needed
USB
Micro-USB — powers board, flashes, provides UART via ST-Link
LD2 (green)
GPIO PA5 — active HIGH, connect to 3.3V through LED+resistor
B1 (blue)
GPIO PC13 — active LOW, internal pull-up, button to GND
Power
5V from USB or VIN (7-12V) — 3.3V regulated on-board
Connectors
Arduino Uno headers + ST Morpho 2x38 pin headers
Nucleo-F334
ST-Link
USB
B1 PC13
LD2 PA5
Arduino
headers
Morpho
pins
B1 is active-LOW (pressed = 0). LD2 is active-HIGH (1 = on). Opposite polarity from ESP32-C3 common-anode LEDs!
Fundamentals of C++ for Microcontrollers | Module 4 | Lesson 12 | 2026

## Slide 10
HAL GPIO API
Reading and writing pins the HAL way
Initialization — GPIO_InitTypeDef
GPIO_InitTypeDef cfg = {0};
cfg.Pin = GPIO_PIN_5; // PA5 = LD2
cfg.Mode = GPIO_MODE_OUTPUT_PP;
cfg.Pull = GPIO_NOPULL;
cfg.Speed = GPIO_SPEED_FREQ_LOW;
HAL_GPIO_Init(GPIOA, &cfg);
Write / Toggle / Read
// Write
HAL_GPIO_WritePin(GPIOA,
GPIO_PIN_5, GPIO_PIN_SET);
// Toggle
HAL_GPIO_TogglePin(GPIOA, GPIO_PIN_5);
// Read
GPIO_PinState st =
HAL_GPIO_ReadPin(GPIOC, GPIO_PIN_13);
if (st == GPIO_PIN_RESET) { /* pressed */ }
GPIO_Mode values
GPIO_MODE_OUTPUT_PP
Push-pull output
Drive HIGH or LOW — most common
GPIO_MODE_OUTPUT_OD
Open-drain output
Needs external pull-up (I2C)
GPIO_MODE_INPUT
Floating input
No pull — external resistor needed
GPIO_MODE_IT_FALLING
Interrupt on fall
Triggers EXTI on HIGH->LOW edge
GPIO_MODE_AF_PP
Alternate function
Pin driven by peripheral (UART, SPI)
Fundamentals of C++ for Microcontrollers | Module 4 | Lesson 12 | 2026

## Slide 11
ESP32-C3 vs STM32F401 — GPIO Comparison
Same concept, different HAL
Topic
ESP32-C3 (Arduino)
STM32F401 (HAL)
LED ON
digitalWrite(3, LOW)
HAL_GPIO_WritePin(GPIOA, PIN_5, SET)
LED toggle
digitalWrite(pin, !state)
HAL_GPIO_TogglePin(GPIOA, PIN_5)
Button read
digitalRead(0) == LOW
HAL_GPIO_ReadPin(GPIOC, PIN_13) == RESET
Delay 500ms
delay(500)
HAL_Delay(500)
Pin config (input)
pinMode(0, INPUT_PULLUP)
cfg.Pull = GPIO_PULLUP + Init()
Pin config (output)
pinMode(3, OUTPUT)
cfg.Mode = OUTPUT_PP + Init()
Flash/debug
USB CDC / PlatformIO upload
ST-Link SWD, CubeIDE
Framework
Arduino Core (C++)
HAL (C) + your C++ on top
The concept is identical — only the function names and register abstraction differ.
Fundamentals of C++ for Microcontrollers | Module 4 | Lesson 12 | 2026

## Slide 12
Demo — Blink LD2 + Read B1
First HAL project on Nucleo-F401RE
What we build:
Create project in CubeMX for NUCLEO-F401RE
Configure PA5 as GPIO_Output (LD2)
Configure PC13 as GPIO_Input pull-up (B1)
Generate code and open in CubeIDE
Write main loop: blink LD2, change rate when B1 pressed
Flash via ST-Link and observe on board
main loop sketch:
/* USER CODE BEGIN 3 */
uint32_t delay_ms = 500;
// Button pressed -> fast blink
if (HAL_GPIO_ReadPin(GPIOC, GPIO_PIN_13)
== GPIO_PIN_RESET) {
delay_ms = 100;
} else {
delay_ms = 500;
}
HAL_GPIO_TogglePin(GPIOA, GPIO_PIN_5);
HAL_Delay(delay_ms);
/* USER CODE END 3 */
Remember:
B1 = active LOW (GPIO_PIN_RESET = pressed) | LD2 = active HIGH (GPIO_PIN_SET = on) | No inversion needed on Nucleo
Fundamentals of C++ for Microcontrollers | Module 4 | Lesson 12 | 2026

## Slide 13
Homework
Extend the demo on your own
1
2
Extend the demo
Add a second blink pattern: SOS in Morse code (... --- ...)
Button B1 switches between normal blink and SOS
Use only HAL_GPIO_TogglePin and HAL_Delay
3
Research
Read: what is SWD (Serial Wire Debug) and how does it differ from JTAG?
Look up: GPIO_PULLUP vs GPIO_NOPULL — when would you use each?
Fundamentals of C++ for Microcontrollers | Module 4 | Lesson 12 | 2026
Install STM32CubeIDE on your machine
Create a new project for NUCLEO-Fxxxx
Verify the project builds and LD2 blinks
Setup

## Slide 14
Summary
What we covered in Lesson 12
F
STM32 family: F0 thru H7, Cortex-M cores, F334 at 84 MHz on Nucleo
E
Ecosystem: CubeMX (config) + CubeIDE (build/debug) + HAL (API)
C
CubeMX generates project skeleton — pinout, clocks, USER CODE sections preserved
P
Project structure: .ioc, Core/Src/main.c, Drivers/ — never edit HAL files
N
Nucleo-F334: PA5 = LD2, PC13 = B1, ST-Link on-board
H
HAL GPIO: WritePin, TogglePin, ReadPin — same concept as ESP32, different names
Next: Lesson 13 — Timers, PWM, and Interrupts on STM32
Fundamentals of C++ for Microcontrollers | Module 4 | Lesson 12 | 2026