## Slide 1
Data Types in C
From Basics to stdint.h
Embedded Systems Course - Lesson 2

## Slide 2
Basic C Data Types
What C provides out of the box
int
Integer numbers (whole numbers)
float / double
Floating-point numbers (decimals)
char
Single character or small integer
bool
Boolean values (true/false)
pointers
Memory addresses
We'll explore each type and their quirks

## Slide 3
Integer Types: int, short, long
int counter = 42; // Standard integer
short small = 100; // Smaller integer
long big = 1000000L; // Larger integer
unsigned int positive = 50; // Only positive (0 and up)
// signed vs unsigned:
int temperature = -10; // Can be negative
unsigned int age = 25; // Never negative
WARNING: Size is platform-dependent!
int could be 2 bytes or 4 bytes depending on your CPU
We'll address this problem soon with stdint.h

## Slide 4
Floating-Point Types: float, double
float temperature = 23.5f; // 32-bit, ~7 decimal digits
double precise = 3.14159265; // 64-bit, ~15 decimal digits
// Always use 'f' suffix for float literals:
float pi = 3.14f; // Correct
float pi = 3.14; // Treated as double, then converted
float (32-bit)
+ Smaller memory
+ Faster operations
- Less precision
- ~7 digits accuracy
double (64-bit)
+ High precision
+ ~15 digits accuracy
- More memory
- Slower on some CPUs

## Slide 5
Float Performance in MCUs
Most microcontrollers lack hardware FPU
Platform | FPU | Float Speed
Arduino (AVR) | NO | ~100x slower (software)
ESP32 | YES | Fast (hardware)
STM32 F4/F7 | YES | Fast (hardware)
STM32 F1/F0 | NO | Slow (software)
RP2040 | NO | Slow (software)
Best Practices for Embedded:
- Avoid float/double when FPU is not available
- Use integer math with scaling (fixed-point)
- Example: temperature * 100 -> store as int (2534 = 25.34C)

## Slide 6
Boolean Type: bool
#include <stdbool.h> // Required in C (C99+)
bool is_ready = true;
bool has_error = false;
// In C++, bool is built-in (no include needed)
// Common usage:
if (is_ready) {
// Do something
}
// Note: Any non-zero value is "true", zero is "false"
int x = 5;
if (x) { // This is true because x != 0
printf("x is non-zero\n");
}
In embedded: bool typically uses 1 byte (8 bits)

## Slide 7
Characters and Strings
char letter = 'A'; // Single character (ASCII)
char digit = '5'; // Character, not number 5!
// Strings = array of characters ending with '\0'
char name[] = "ESP32"; // Actually: {'E','S','P','3','2','\0'}
char buffer[20] = "Hello"; // Fixed size buffer
// String operations:
strlen(name); // Length: 5 (not counting \0)
strcpy(buffer, "World"); // Copy string
strcat(buffer, "!"); // Concatenate
IMPORTANT: Strings in C are NOT objects like in Python/Java! They're just arrays of characters with a null terminator (\0)

## Slide 8
Pointers: Memory Addresses
int value = 42;
int *ptr = &value; // ptr holds the address of value
printf("%d\n", value); // Prints: 42
printf("%d\n", *ptr); // Prints: 42 (dereference)
printf("%p\n", ptr); // Prints: memory address
*ptr = 100; // Changes value through pointer
printf("%d\n", value); // Now prints: 100
Pointer operators:
& = address-of
* = dereference -> = access member
Common uses: - Pass by reference - Dynamic memory - Hardware registers

## Slide 9
The Problem: What's Wrong with int?
int counter = 100;
int temperature = -40;
int sensor_data = 0xFF;
// How many bytes is this?
The Problems: - Size depends on platform - 16 bits on AVR Arduino - 32 bits on ESP32/STM32 - 64 bits on some systems
Result: unpredictable behavior!
We need a way to guarantee the size!

## Slide 10
int Size Across Platforms
Platform | sizeof(int) | Range
Arduino (AVR) | 2 bytes | -32768 to 32767
ESP32 (Xtensa) | 4 bytes | -2147483648 to 2147483647
STM32 (ARM) | 4 bytes | -2147483648 to 2147483647
RP2040 (ARM) | 4 bytes | -2147483648 to 2147483647
Linux x86_64 | 4 bytes | -2147483648 to 2147483647
WARNING: Same code can behave differently!

## Slide 11
The Solution: stdint.h
C99 Standard with Fixed-Width Types
#include <stdint.h>
uint8_t counter = 0; // ALWAYS 8 bits (1 byte)
int16_t temperature = -40; // ALWAYS 16 bits (2 bytes)
uint32_t timestamp = 0; // ALWAYS 32 bits (4 bytes)
// Works identically on:
// - ESP32 - STM32 - Arduino - RP2040
Guaranteed size on any platform!

## Slide 12
stdint.h Types: Complete Set
Unsigned (no sign)
uint8_t // 0 to 255
uint16_t // 0 to 65535
uint32_t // 0 to 4294967295
uint64_t // 0 to 18+ quintillion
// Use for:
// - counters
// - array indices
// - bit masks
Signed (with sign)
int8_t // -128 to 127
int16_t // -32768 to 32767
int32_t // -2147483648 to ...
int64_t // huge range
// Use for:
// - temperature
// - coordinates
// - differences
Rule: if no negatives needed, use unsigned!

## Slide 13
How to Choose the Right Type?
Value always >= 0?
=> Use uint_
Range up to 255?
=> uint8_t
Range up to 65535?
=> uint16_t
Need negatives?
=> int8_t/16_t/32_t
In embedded: save memory - choose smallest suitable size!

## Slide 14
The sizeof() Operator
Check the size of a type in bytes
#include <stdint.h>
#include <stdio.h>
uint8_t a = 42;
uint16_t b = 1000;
uint32_t c = 1000000;
printf("uint8_t: %lu bytes\n", sizeof(a)); // 1
printf("uint16_t: %lu bytes\n", sizeof(b)); // 2
printf("uint32_t: %lu bytes\n", sizeof(c)); // 4
// Or check type directly:
printf("Size: %lu\n", sizeof(uint32_t)); // 4
Useful for debugging and verifying sizes!

## Slide 15
Overflow: Type Wrap-Around
uint8_t counter = 253;
counter++; // 254
counter++; // 255
counter++; // 0 <-- wraps around!
counter++; // 1
counter++; // 2
// uint8_t: 0-255, then back to 0
What happens:
253 -> 254 -> 255 -> 0
Maximum reached!
Signed type (int8_t):
127 -> -128
WARNING: Be careful with range boundaries!

## Slide 16
Type Casting: Converting Types
// Data loss when downsizing
uint16_t big = 1000;
uint8_t small = big; // small = 232 (data loss!)
// 1000 = 0x03E8
// uint8_t takes only lower byte: 0xE8 = 232
// Explicit casting
int16_t temp = -10;
uint16_t positive = (uint16_t)temp; // 65526 (wrong!)
// Negative value becomes huge unsigned number!
Always think about ranges when casting types!

## Slide 17
Best Practices for Embedded
YES
Always use stdint.h
Guaranteed sizes
YES
Choose smallest type
uint8_t over uint32_t when possible
YES
Unsigned by default
If no negatives needed
YES
Check boundaries
Avoid overflow/underflow
NO
Don't use int/long
Size depends on platform
NO
Don't cast blindly
Can lose data

## Slide 18
Summary
C provides basic types: int, float, char, bool, pointers Problem: int size varies by platform
Solution: Use stdint.h for guaranteed sizes
Remember overflow and casting pitfalls!
Next: Practice with ESP32!