## Slide 1
LESSON 10
Analog Input
& RGB Control
Potentiometer class | RgbLed class | Library design patterns
Fundamentals of C++ for Microcontrollers | ESP32-C3

## Slide 2
Lesson 10 — Agenda
01
ADC Fundamentals
How analogRead() works on ESP32-C3, 12-bit resolution
02
Potentiometer Class
Inheriting from AnalogPin, readRaw() and readPercent()
03
Demo 1: Brightness
Potentiometer controls LED brightness via PwmPin
04
RgbLed Class
Composition: three PwmPin members, setColor(r,g,b)
05
Demo 2: Color Zones
0-33% Red, 34-66% Green, 67-100% Blue
06
Pitfalls & Best Practices
ADC noise, map() vs constrain(), polling vs ISR

## Slide 3
Recap: Class Hierarchy from Lesson 9
DigitalPin
base class
Button
input
Led
output
AnalogPin
base class
? NEW
Potentiometer
PwmPin
PWM output
Potentiometer <-- NEW
RgbLed
NEW
RgbLed <-- NEW
Today we add two new classes to our driver library

## Slide 4
ADC on ESP32-C3
12-bit resolution
0 to 4095 raw counts
Input voltage range
0 V to 3.3 V (do not exceed!)
Reference voltage
Internal 3.3 V (no external VREF needed)
ADC channels
GPIO 0-5 on ESP32-C3 (ADC1)
analogRead() return
uint16_t, 0..4095
Sampling
Blocking call — ~10 us, call from loop()
Voltage -> Raw Value
3.3 V
4095
2.475 V
3071
1.65 V
2047
0.825 V
1023
0.0 V
0

## Slide 5
Potentiometer Class — Design
Potentiometer
inherits: AnalogPin
- _resolution : uint16_t
+ Potentiometer(pin: uint8_t)
+ readRaw() : uint16_t
+ readPercent() : uint8_t
+ map(outMin, outMax) : int32_t
Inheritance
Potentiometer extends AnalogPin.
All pin setup is handled by the base class.
readRaw()
Returns 0..4095 directly from analogRead().
No filtering — raw hardware value.
readPercent()
Maps raw 0..4095 to 0..100.
Uses integer arithmetic only.
map()
General-purpose scaler.
Converts potentiometer range to any output range.

## Slide 6
Potentiometer Class — Code
Potentiometer.h
#pragma once
#include <stdint.h>
#include "AnalogPin.h"
namespace drivers {
class Potentiometer : public AnalogPin {
public:
explicit Potentiometer(uint8_t pin);
uint16_t readRaw() const;
uint8_t readPercent() const;
int32_t map(int32_t outMin,
int32_t outMax) const;
};
} // namespace drivers
Potentiometer.cpp
#include "Potentiometer.h"
#include <Arduino.h>
namespace drivers {
Potentiometer::Potentiometer(uint8_t pin)
: AnalogPin(pin) {}
uint16_t Potentiometer::readRaw() const {
return analogRead(_pin);
}
uint8_t Potentiometer::readPercent() const {
return (uint8_t)(readRaw() * 100UL
/ 4095UL);
}
int32_t Potentiometer::map(
int32_t outMin,
int32_t outMax) const {
return ::map(readRaw(),
0, 4095,
outMin, outMax);
}
} // namespace drivers

## Slide 7
Demo 1 — Potentiometer Controls LED Brightness
Potentiometer
GPIO (ADC pin)
readRaw()
0 .. 4095
map()
0 .. 255
PwmPin
setBrightness()
LED
dim .. bright
Wiring
Potentiometer pin
Constructor arg (e.g. GPIO 2)
Pot VCC
3.3 V
Pot GND
GND
Red LED (active-low)
GPIO 3 (existing)
Key Concept
analogRead() returns 12-bit value (0-4095)
PWM duty cycle expects 8-bit value (0-255)
Arduino map() converts between ranges
Red LED is active-low: invert the value!
No ISR needed -- polling in loop() is correct

## Slide 8
Demo 1 — Code: main.cpp
#include <Arduino.h>
#include "Potentiometer.h"
#include "Led.h"
using namespace drivers;
// GPIO 2 = ADC-capable pin on ESP32-C3
static Potentiometer pot(2);
// GPIO 3, active-low (common anode)
static Led led(3, true);
void setup() {
Serial.begin(115200);
}
void loop() {
uint16_t raw = pot.readRaw();
uint8_t pct = pot.readPercent();
// map 0..4095 -> 0..255 for PWM
int32_t duty = pot.map(0, 255);
// active-low: 255=off, 0=full brightness
uint8_t inv = (uint8_t)(255 - duty);
led.setBrightness(inv);
Serial.print("Raw: "); Serial.print(raw);
Serial.print(" %: "); Serial.println(pct);
delay(20);
}
Include our new class
Static allocation -- no heap
12-bit -> 8-bit scaling
Invert for active-low LED
Debug output to Serial Monitor

## Slide 9
RgbLed Class — Design
RgbLed
inherits: Led (which inherits: PwmPin)
- _red : PwmPin
- _green : PwmPin
- _blue : PwmPin
+ RgbLed(rPin, gPin, bPin : uint8_t)
+ setColor(r, g, b : uint8_t)
+ off()
Design Note: Composition
RgbLed HAS three PwmPin members (composition),
not IS-A PwmPin (inheritance).
An RGB LED is three independent PWM channels.
Composition models this more accurately.
Inherits from Led
RgbLed extends Led so it also acts as a
single-channel LED (the red channel).
Students see two-level hierarchy in action.
setColor(r,g,b)
Takes three uint8_t values (0-255).
Each value drives one PwmPin channel.
Common cathode: higher = brighter.
off()
Calls setBrightness(0) on all three
channels. Clean one-liner for students.

## Slide 10
RgbLed Class — Code
RgbLed.h
#pragma once
#include <stdint.h>
#include "Led.h"
#include "PwmPin.h"
namespace drivers {
class RgbLed : public Led {
public:
RgbLed(uint8_t rPin,
uint8_t gPin,
uint8_t bPin);
void setColor(uint8_t r,
uint8_t g,
uint8_t b);
void off();
private:
PwmPin _green;
PwmPin _blue;
// _red channel is inherited Led
};
} // namespace drivers
RgbLed.cpp
#include "RgbLed.h"
namespace drivers {
RgbLed::RgbLed(uint8_t rPin,
uint8_t gPin,
uint8_t bPin)
: Led(rPin),
_green(gPin),
_blue(bPin) {}
void RgbLed::setColor(uint8_t r,
uint8_t g,
uint8_t b) {
setBrightness(r); // inherited
_green.write(g);
_blue.write(b);
}
void RgbLed::off() {
setColor(0, 0, 0);
}
} // namespace drivers

## Slide 11
Demo 2 — Color Zones: Concept
0%
33%
34%
66%
67%
100%
RED
GREEN
BLUE
Zone Logic
Zone
Percent range
setColor(r, g, b)
RED
0 .. 33
setColor(255, 0, 0)
GREEN
34 .. 66
setColor(0, 255, 0)
BLUE
67 .. 100
setColor(0, 0, 255)
Implementation Notes
Read pot.readPercent() in loop()
Use if / else-if chain for zones
No need for map() -- just compare
Common cathode: no inversion needed
Serial.println() the zone name for debug

## Slide 12
Demo 2 — Code: main.cpp
#include <Arduino.h>
#include "Potentiometer.h"
#include "RgbLed.h"
using namespace drivers;
static Potentiometer pot(2);
// Common cathode: R=GPIO6, G=GPIO7, B=GPIO8
static RgbLed rgb(6, 7, 8);
void setup() {
Serial.begin(115200);
}
void loop() {
uint8_t pct = pot.readPercent();
if (pct <= 33) {
rgb.setColor(255, 0, 0); // RED
Serial.println("Zone: RED");
} else if (pct <= 66) {
rgb.setColor(0, 255, 0); // GREEN
Serial.println("Zone: GREEN");
} else {
rgb.setColor(0, 0, 255); // BLUE
Serial.println("Zone: BLUE");
}
delay(50);
}
Zone: RED
pct 0..33
setColor(255,0,0)
Zone: GREEN
pct 34..66
setColor(0,255,0)
Zone: BLUE
pct 67..100
setColor(0,0,255)

## Slide 13
Full Class Hierarchy — After Lesson 10
DigitalPin
base
AnalogPin
base
PwmPin
base
Button
input
Led
output
Potentiometer
NEW
RgbLed
NEW
HAS 2x PwmPin (composition)
= inheritance
= composition
= new this lesson

## Slide 14
Pitfalls & Best Practices
!
ADC Noise & Jitter
analogRead() on ESP32-C3 has ~5-10 LSB noise at rest.
LED may flicker at zone boundaries. Fix: add deadband or
average multiple readings.
uint16_t avg = 0;
for(uint8_t i=0;i<8;i++) avg+=analogRead(_pin);
avg /= 8;
!
map() Does Not Clamp
Arduino map() returns values outside [outMin,outMax]
if input exceeds [inMin,inMax]. Always constrain() first.
uint16_t raw = constrain(readRaw(), 0, 4095);
int32_t duty = ::map(raw, 0, 4095, 0, 255);
!
analogRead() Inside ISR
Never call analogRead() from an ISR on ESP32.
It is a blocking operation that uses the SAR ADC
peripheral. Use a timer flag + poll in loop() instead.
// WRONG:
void IRAM_ATTR onTimer() { analogRead(pin); }
// CORRECT: set flag, read in loop()
!
Zone Boundary Flicker
At exactly 33% or 66%, noise causes rapid color
switching. Add a +/-1% hysteresis band to fix.
// simple hysteresis example:
if(pct < 32) { /* RED */ }
else if(pct > 34) { /* check next zone */ }

## Slide 15
Common Cathode vs Common Anode
Common Cathode
(this lesson -- RGB LED)
Shared GND pin (-)
PWM signal on R, G, B pins
write(255) = full brightness
write(0) = LED off
setColor(255,0,0) = RED fully on
// Common cathode
rgb.setColor(255, 0, 0); // RED on
Common Anode
(red LED on GPIO 3)
Shared VCC pin (+)
PWM signal on R, G, B pins
write(0) = full brightness
write(255) = LED off
Must invert: inv = 255 - duty
// Common anode (active-low)
uint8_t inv = 255 - duty;
led.setBrightness(inv);
Rule of thumb: check your RGB LED datasheet, or simply test -- if colors are inverted, swap your logic.

## Slide 16
Lesson 10 — Summary
1
ADC Fundamentals
12-bit resolution, 0-4095, polling-only.
Never call analogRead() from ISR.
2
Potentiometer Class
Inherits AnalogPin. Adds readRaw(),
readPercent(), and map() helpers.
3
Demo 1: Brightness
map() converts 12-bit to 8-bit PWM range.
Active-low LED needs value inversion.
4
RgbLed Class
Inherits Led. Adds two PwmPin members
by composition. setColor(r,g,b) API.
5
Demo 2: Color Zones
if/else chain on readPercent().
Three distinct color regions on the dial.
6
Pitfalls
ADC noise, map() clamping, zone
boundary hysteresis -- test on hardware!

## Slide 17
Questions?
Lesson 10 covered:
Potentiometer class (inherits AnalogPin)
RgbLed class (inherits Led, composition of PwmPin)
Demo 1: brightness control
Demo 2: three-zone color display
Fundamentals of C++ for Microcontrollers | ESP32-C3 | Lesson 10