## Slide 1
MODULE 4 — MICROCONTROLLER PLATFORMS
Lesson 14
Nokia 5110 LCD via SPI
on NUCLEO-F446RE
SPI Protocol
PCD8544 Driver
Bitmap Font
HAL_SPI_Transmit

## Slide 2
SPI — Serial Peripheral Interface
A synchronous serial bus: full-duplex, master-driven, 4-wire
SCK
Clock — generated by master, synchronises every bit
MOSI
Master Out Slave In — data from STM32 to display
MISO
Master In Slave Out — not used (PCD8544 is write-only)
CS
Chip Select — active-low, enables the device
SPI Key Properties
Clock polarity: CPOL=0
Clock phase: CPHA=0 (Mode 0)
Bit order: MSB first
Data width: 8 bits
Max speed: 4 MHz (PCD8544)
Nokia 5110 uses 3 of 4 wires:
SCK + MOSI + CS
Plus DC pin (command/data)

## Slide 3
PCD8544 — Nokia 5110 LCD Controller
84 x 48 pixels, monochrome, 3.3 V logic, SPI-only (no MISO)
Pin | Name | Function
RST | Reset | Active-low hardware reset
CE | Chip Enable | SPI chip select (active-low)
DC | Data/Command | LOW = command, HIGH = data
DIN | MOSI | SPI data input to display
CLK | SCK | SPI clock
VCC | Power | 3.3 V (max 3.6 V — do not use 5 V!)
LIGHT | Backlight | LED anode — connect via resistor to GND
GND | Ground | Reference ground
WARNING VCC must be 3.3 V. The F446RE GPIO is 3.3 V — safe. Never connect to 5 V header pins.

## Slide 4
Wiring — F446RE to Nokia 5110
SPI1 peripheral + four GPIO control lines
Nokia 5110 | F446RE Pin | Signal
VCC | 3.3V | Power
GND | GND | Ground
CLK | PA5 (D13) | SPI1_SCK
DIN | PA7 (D11) | SPI1_MOSI
CE | PB6 (D10) | GPIO out (NSS SW)
DC | PA9 (D8) | GPIO out
RST | PA8 (D7) | GPIO out
LIGHT | GND | Backlight (always on)
Notes
SPI1: hardware SCK
and MOSI only.
No MISO needed.
CE / DC / RST are
plain GPIO outputs
(push-pull, no AF).
LIGHT -> GND works
if module has a resistor.

## Slide 5
STM32CubeMX — SPI1 Configuration
Peripheral setup before writing a single line of driver code
SPI1 Settings
Mode: Full-Duplex Master
Data Size: 8 Bits
First Bit: MSB First
CPOL: Low (CPOL=0)
CPHA: 1 Edge (CPHA=0)
NSS: Software
Baud Rate: APB2/16 (~5.6 MHz)
GPIO Pins (Output, Push-Pull)
PB6 -> Nokia CE (label: LCD_CE)
PA9 -> Nokia DC (label: LCD_DC)
PA8 -> Nokia RST (label: LCD_RST)
Setup Steps
1. Open .ioc in STM32CubeIDE
2. Pinout -> SPI1 -> Full-Duplex Master
3. PA5 = SPI1_SCK, PA7 = SPI1_MOSI
4. NSS = Software (we toggle PB6 manually)
5. Set PB6, PA9, PA8 as GPIO_Output
6. Label them in Pin properties
7. Project -> Generate Code

## Slide 6
PCD8544 Protocol — Command vs Data
The DC pin tells the controller whether each SPI byte is a command or pixel data
DC = 0
COMMAND byte — configures the controller
(contrast, addressing mode, display on/off)
DC = 1
DATA byte — pixel data written to DDRAM
(each bit = one pixel in the 84x6-row grid)
Initialization Sequence
// 1. Toggle RST low then high
HAL_GPIO_WritePin(LCD_RST_GPIO, 0);
HAL_Delay(1);
HAL_GPIO_WritePin(LCD_RST_GPIO, 1);
// 2. Enter extended command mode
lcd_cmd(0x21); // PD=0, V=0, H=1
lcd_cmd(0xB8); // Vop (contrast)
lcd_cmd(0x04); // Temp coeff
lcd_cmd(0x14); // Bias 1:48
// 3. Enter basic mode, display on
lcd_cmd(0x20);
lcd_cmd(0x0C); // Normal mode
DDRAM Layout
84 columns x 6 banks
Each bank = 8 pixel rows
= 84 x 48 = 4032 pixels
Address auto-increments
left-to-right, then next
bank (horizontal mode).
Clear = write 504 zeros.

## Slide 7
Text Rendering — 5x7 Bitmap Font
Each ASCII character is stored as 5 bytes, one byte per column of pixels
Character 'A' (ASCII 65) = 5 column bytes:
0x7E
0x11
0x11
0x11
0x7E
bit 0 (top)
bit 7 (bottom)
// Font table entry for 'A'
static const uint8_t font5x7[][5] = {
// ... (index = ASCII - 0x20)
{ 0x7E, 0x11, 0x11, 0x11, 0x7E }, // 'A'
};
print_char()
1. Lookup char in font[][]
2. Set DC = HIGH (data)
3. SPI-transmit 5 bytes
4. Send 1 spacer byte 0x00
(6 bytes per character)
print_string() loops
print_char() for each
character in the string.

## Slide 8
Demo — Counter on Nokia 5110
Three layers: HAL SPI -> PCD8544 driver -> application
Application
main.c — counter, sprintf, lcd_print_string()
PCD8544 Driver
lcd_init / lcd_clear / lcd_goto / lcd_print_char
STM32 HAL
HAL_SPI_Transmit / HAL_GPIO_WritePin / HAL_Delay
uint32_t counter = 0;
char buf[16];
while (1) {
sprintf(buf, "Count: %5lu", counter++);
lcd_goto(0, 2); // col=0, bank=2
lcd_print_string(buf);
HAL_Delay(500);
}
lcd_send_byte() helper
void lcd_send_byte(
uint8_t data,
uint8_t is_data)
{
// Set DC pin
HAL_GPIO_WritePin(DC_PORT,
DC_PIN,
is_data ? GPIO_PIN_SET
: GPIO_PIN_RESET);
// Assert CE
HAL_GPIO_WritePin(CE_PORT,
CE_PIN, GPIO_PIN_RESET);
// Transmit 1 byte
HAL_SPI_Transmit(&hspi1,
&data, 1, HAL_MAX_DELAY);
// Release CE
HAL_GPIO_WritePin(CE_PORT,
CE_PIN, GPIO_PIN_SET);
}

## Slide 9
Homework — Simple LCD UI
Extend the demo: display a multi-line dashboard that updates on a timer
Requirements
1. Display exactly 3 lines:
Line 1: static label
e.g. 'STM32 F446RE'
Line 2: uptime in seconds
use HAL_GetTick()/1000
Line 3: a counter (free choice)
2. Update every 1 second
(compare HAL_GetTick() ticks,
do NOT use HAL_Delay in loop)
3. No screen flicker:
only redraw changed lines
Hints
lcd_goto(col, bank) sets
the DDRAM cursor position.
bank 0..5, col 0..83.
Non-blocking timer pattern:
uint32_t last = 0;
if (HAL_GetTick()-last>=1000){
last = HAL_GetTick();
// update display
}
sprintf(buf, ...) converts
numbers to strings.
Pad with spaces to erase
leftover digits.

## Slide 10
Available PCD8544 Libraries for STM32
Writing your own driver teaches the protocol. Libraries save time in production.
STM32-HAL-Nokia-5110
alireza-tabatabaee (port of Tilen Majerle)
github.com/alireza-tabatabaee/STM32-HAL-Nokia-5110-library
HAL + CubeMX compatible
Hardware SPI (fast)
5x7 font included
Simple 3-function API
Best match for this course
stm32-hal-pcd8544
henriheimann
github.com/henriheimann/stm32-hal-pcd8544
Handle-based (no globals)
504-byte back buffer
Draw pixels / lines
Modern C style
Cleaner architecture
u8g2
olikraus
github.com/olikraus/u8g2
Supports 100+ displays
Full graphics API
Many font sizes
Cross-platform
Overkill for Nokia 5110

## Slide 11
Using a Ready-Made Library — Example
alireza-tabatabaee/STM32-HAL-Nokia-5110: drop-in replacement for our driver
Integration Steps
1. Download stm32f4_pcd8544.h
and stm32f4_pcd8544.c
from GitHub
2. Copy both files into
Core/Inc and Core/Src
3. Edit the top of .h:
set SPI handle and
GPIO port/pin defines
4. Replace our driver calls
with library API
(see code on the right)
5. Build -- no other changes
Step 3 -- configure the header
extern SPI_HandleTypeDef hspi1;
#define PCD8544_SPI hspi1
#define PCD8544_RST_PORT LCD_RST_GPIO_Port
#define PCD8544_RST_PIN LCD_RST_Pin
#define PCD8544_CE_PORT LCD_CE_GPIO_Port
#define PCD8544_CE_PIN LCD_CE_Pin
#define PCD8544_DC_PORT LCD_DC_GPIO_Port
#define PCD8544_DC_PIN LCD_DC_Pin
Step 4 -- API comparison
Our driver
lcd_init(&hspi1,
0xB8);
lcd_goto(0, 2);
lcd_print_string(
buf);
lcd_clear();
Library
PCD8544_Init(
0x38);
PCD8544_GotoXY(0,2);
PCD8544_Puts(
buf, ...);
PCD8544_Refresh();
PCD8544_Clear();
Key difference: library uses a back buffer -- you must call Refresh() to push changes to the display.

## Slide 12
Lesson 14 — Key Takeaways
SPI
SPI is a 4-wire synchronous bus. PCD8544 only needs SCK + MOSI + CE (plus DC for command/data).
HAL
HAL_SPI_Transmit() is blocking (polling mode) — simple, predictable, ideal for learning.
DC
The DC pin is unique to PCD8544: pull LOW before sending commands, HIGH before sending pixel data.
FONT
Text is rendered via a 5x7 pixel bitmap font. Each character = 5 SPI bytes + 1 spacer.
TICK
HAL_GetTick() returns milliseconds since reset — use it for non-blocking periodic updates.
Next: Module 4 continues — RP2040 platform overview