## Slide 1
Lesson 3
Control Flow, Functions & Pointers
Embedded Systems Development

## Slide 2
Today's Agenda
01
Conditions
if/else, switch/case, ternary operator
02
Loops
for, while, do-while, infinite loops in embedded
03
Functions
Declaration, parameters, return values
04
Pointers Introduction
Addresses, dereferencing, why it matters
05
Practice: Button Input
Push button + debounce + serial counter

## Slide 3
Conditional Statements: if / else
int temp = readSensor();
if (temp > 50) {
printf("DANGER!\n");
} else if (temp > 30) {
printf("Warning\n");
} else {
printf("Normal\n");
}
Key Rules
Condition must be in parentheses ()
Braces {} define the code block
else if chains for multiple checks
else is optional (default case)
Common Bug!
if (x = 5) -- assignment, always true!
if (x == 5) -- comparison, correct
Ternary: int max = (a > b) ? a : b; // compact single-line if/else

## Slide 4
switch / case Statement
switch (state) {
case STATE_IDLE:
ledOff();
break;
case STATE_RUNNING:
ledBlink();
break;
case STATE_ERROR:
ledOn();
break;
default:
break;
}
When to Use
Comparing ONE variable to multiple values
State machines (very common in embedded!)
Menu systems, command parsers
Cleaner than long if/else if chains
Do NOT forget break;
Without break, execution "falls through" to the next case -- a classic C bug.
switch only works with integer/char types -- not strings or floats!

## Slide 5
Loops: for
for (int i = 0; i < 10; i++)
init
condition
increment
Runs once
before loop
Checked before
each iteration
Runs after
each iteration
// Print 0 to 9
for (int i = 0; i < 10; i++) {
printf("%d\n", i);
}
// Nested loops (2D array)
for (int r = 0; r < 3; r++) {
for (int c = 0; c < 3; c++)
printf("%d ", grid[r][c]);
}
break; -- exit the loop immediately
continue; -- skip to next iteration

## Slide 6
Loops: while & do-while
while
Check condition FIRST, then execute
int count = 0;
while (count < 5) {
doSomething();
count++;
}
do-while
Execute FIRST, then check condition
int input;
do {
input = readButton();
} while (input == 0);
Infinite Loops in Embedded Systems
while (1) { ... }
for (;;) { ... }
In embedded, your program runs FOREVER. The main loop is always infinite. Arduino's loop() function is called inside while(1) by the framework.

## Slide 7
Functions: Declaration & Definition
int add(int a, int b) { return a + b; }
return
type
function
name
parameters
body
void function (no return)
void blinkLed(int pin) {
digitalWrite(pin, HIGH);
delay(500);
digitalWrite(pin, LOW);
delay(500);
}
Function with return value
float celsiusToF(float c) {
return c * 1.8 + 32.0;
}
// Usage:
float f = celsiusToF(25.0);
In C: function prototypes must appear before usage, or define functions above main()

## Slide 8
Why Use Functions?
Reusability
Write once, call many times. blinkLed() works for any pin.
Readability
Named functions explain WHAT the code does. Self-documenting.
Testability
Small functions are easy to test independently.
Maintainability
Fix a bug in one place, not copy-pasted in 10 places.
Rule of thumb: if you copy-paste code, make it a function!

## Slide 9
Pointers: What Are They?
A pointer is a variable that stores a memory address
0x1000
42
x
0x1004
7
y
0x1008
0x1000
ptr
-->
int x = 42;
int* ptr = &x; // ptr stores ADDRESS of x
printf("%d\n", *ptr); // prints 42 (dereference)
*ptr = 99; // x is now 99!

## Slide 10
Pointer Operators: & and *
& Address-of operator
"Give me the ADDRESS where this variable lives"
int x = 42;
int* ptr = &x;
// ptr now holds 0x1000
// (address of x in memory)
* Dereference operator
"Give me the VALUE at the address this pointer holds"
printf("%d", *ptr); // 42
*ptr = 99; // x = 99
// Changed x through pointer!
NULL Pointers -- Always Check!
int* ptr = NULL; // Points to nothing
if (ptr != NULL) { // ALWAYS check before using!
value = *ptr; }

## Slide 11
Why Pointers Matter in Embedded
Hardware Register Access
Peripherals (GPIO, UART, SPI) are mapped to specific memory addresses. Pointers let you read/write hardware directly.
volatile uint32_t* gpio = (uint32_t*)0x60004004;
Pass by Reference
C only passes by value. Pointers let functions modify the caller's variables without copying large data.
void readSensor(int* temperature, int* humidity);
Dynamic Data & Buffers
Working with arrays, strings, and communication buffers requires pointer manipulation.
char buffer[64]; char* ptr = buffer;
We will dive deeper into pointers in future lessons!

## Slide 12
printf Format Specifiers
Specifier | Type | Example | Output
%d | Decimal integer | printf("%d", 42) | 42
%o | Octal | printf("%o", 42) | 52
%x / %X | Hexadecimal | printf("%X", 255) | FF
%f | Float / double | printf("%.2f", 3.14) | 3.14
%c | Character | printf("%c", 65) | A
%s | String | printf("%s", "hi") | hi
Width & Padding (important for tables!)
printf("%4d", 42); // " 42" (right-aligned, width 4)
printf("%-4d", 42); // "42 " (left-aligned)
printf("%04X", 255); // "00FF" (zero-padded hex)

## Slide 13
PRACTICE
Button Input + Serial Counter
Wiring (ESP32-C3 Super Mini)
Button Pin 1 --> GPIO 3
Button Pin 2 --> GND
No external resistor needed!
We use INPUT_PULLUP mode:
Not pressed = HIGH (1)
Pressed = LOW (0)
Note: logic is INVERTED
compared to what you expect!
What We Will Build
1. Read button state
2. Debounce (filter noise)
3. Count presses
4. Print counter to Serial
Topics covered:
if/else -- button state check
while(1) -- main loop (loop())
functions -- debounce logic
Serial.printf() -- formatted output

## Slide 14
Step 1: Basic Button Read
#define BUTTON_PIN 3
int counter = 0;
int lastState = HIGH; // pullup = HIGH when not pressed
void setup() {
Serial.begin(115200);
pinMode(BUTTON_PIN, INPUT_PULLUP);
}
void loop() {
int currentState = digitalRead(BUTTON_PIN);
if (currentState == LOW && lastState == HIGH) {
counter++;
Serial.printf("Button pressed! Count: %d\n", counter);
}
lastState = currentState;
}

## Slide 15
Step 2: Add Debounce
Why Debounce?
Mechanical buttons "bounce" -- the contacts physically vibrate for a few milliseconds. One press can register as 5-10 presses without debouncing.
Simple Fix: delay()
After detecting a press, wait 50ms and ignore further changes. Simple but blocks the CPU -- fine for learning, not ideal for production.
#define DEBOUNCE_MS 50
bool isButtonPressed() {
int reading = digitalRead(BUTTON_PIN);
if (reading == LOW && lastState == HIGH) {
delay(DEBOUNCE_MS); // wait for bounce to settle
reading = digitalRead(BUTTON_PIN); // read again
lastState = reading;
return (reading == LOW); // true if still pressed
}
lastState = reading;
return false;

## Slide 16
Homework Assignment
Multiplication Table 16x16
Print a 16x16 multiplication table to Serial Monitor using Serial.printf()
Use a push button to cycle between number systems: OCT -> DEC -> HEX -> OCT ...
Format output with fixed-width columns using printf width specifiers
Reprint the entire table each time the button is pressed
Requirements
Use nested for loops for table
Use switch/case for mode select
Extract print logic into a function
Debounce the button
Aligned columns (printf width)
Hints
// OCT:
Serial.printf("%6o", val);
// DEC:
Serial.printf("%4d", val);
// HEX:
Serial.printf("%4X", val);

## Slide 17
Lesson 3 Summary
Conditions
if/else for decisions, switch/case for state machines
Loops
for (counted), while (conditional), infinite loops in embedded
Functions
Reusable code blocks with parameters and return values
Pointers
Variables that store memory addresses -- & and * operators
printf
Format specifiers: %d, %o, %x, %f with width control
Button Input
INPUT_PULLUP, debounce, edge detection
Next: Arrays, Strings & Memory Layout

## Slide 18
Questions?
See you next session
Homework: 16x16 Multiplication Table with OCT/DEC/HEX modes