## Slide 1
LESSON 04
Structs and
Pointers to Structs
Grouping data • Memory layout • Arrow operator • Embedded patterns
Embedded Systems Course 2026 | ESP32-C3 / PlatformIO

## Slide 2
What We Will Cover Today
01
Struct basics
Defining, initializing, and accessing members
02
Memory layout
How structs live in RAM — alignment and padding
03
Pointers to structs
& operator, -> operator, passing by pointer
04
Embedded patterns
GPIO descriptor, peripheral config, driver structs
05
Hands-on exercise
Build a button driver using a struct + pointer

## Slide 3
What Is a Struct?
A struct bundles multiple variables of different types under one name.
Think of it as a custom data type that models a real-world object.
In embedded systems, structs represent hardware registers, peripheral configs, sensor readings, and protocol frames.
Structs keep related data together — improving readability and enabling clean driver APIs.
// Modeling a GPIO pin
struct GpioPin {
uint8_t pin_num;
bool is_output;
bool active_high;
};
// Creating an instance
struct GpioPin led;
led.pin_num = 8;
led.is_output = true;
led.active_high = true;
// Accessing a member
if (led.is_output) {
gpio_set(led.pin_num, 1);
}

## Slide 4
Memory Layout of a Struct
pin_num
uint8_t
pad
is_output
bool
pad
active_high
bool
pad
Byte: 0 1 2 3 4 5 6 7 8
Note: The compiler may insert padding bytes to align members on natural boundaries (e.g. a uint32_t wants to start at an address divisible by 4). Use __attribute__((packed)) to disable padding — but be aware of performance trade-offs on RISC-V (ESP32-C3).
// Check size at compile time
static_assert(sizeof(struct GpioPin) == 3, "Unexpected padding!");
// Packed: no padding, useful for protocol frames / register maps
struct __attribute__((packed)) SpiFrame { uint8_t cmd; uint16_t addr; uint32_t data; };

## Slide 5
Pointers to Structs
Two ways to access members:
.
Dot operator
Direct variable
pin.pin_num
->
Arrow operator
Pointer to struct
p->pin_num
p->member is shorthand for (*p).member
struct GpioPin led = {
.pin_num = 8,
.is_output = true,
.active_high = true,
};
// Pointer to the struct
struct GpioPin *p = &led;
// Three equivalent accesses:
uint8_t a = led.pin_num; // dot
uint8_t b = (*p).pin_num; // deref+dot
uint8_t c = p->pin_num; // arrow (preferred)
// Pass to a function by pointer
void gpio_init(struct GpioPin *pin) {
pinMode(pin->pin_num,
pin->is_output ? OUTPUT : INPUT);
}
gpio_init(&led);

## Slide 6
Passing Structs: By Value vs By Pointer
By Value (AVOID for structs)
void init_val(struct GpioPin pin) {
// 'pin' is a full COPY
// Changes do NOT affect caller
pin.is_output = true; // lost!
}
Copies all bytes of the struct
Expensive for large structs
Original is never modified
Rarely useful in embedded drivers
By Pointer (PREFERRED)
void init_ptr(struct GpioPin *pin) {
// 'pin' is a 4-byte pointer
// Changes DO affect caller
pin->is_output = true; // works!
pinMode(pin->pin_num, OUTPUT);
}
Only 4 bytes copied (pointer size)
Zero copy overhead — always fast
Caller's struct IS modified
Standard pattern in embedded C drivers

## Slide 7
Embedded Pattern: GPIO Pin Descriptor
ESP32-C3 — PlatformIO / Arduino Framework
// gpio_driver.h
#include <stdint.h>
#include <stdbool.h>
#include <Arduino.h>
typedef struct {
uint8_t pin;
bool output;
bool active_high;
bool pull_up;
} GpioPin_t;
// Driver API
void gpio_pin_init(GpioPin_t *p);
void gpio_pin_set(GpioPin_t *p, bool state);
bool gpio_pin_read(GpioPin_t *p);
// gpio_driver.cpp
void gpio_pin_init(GpioPin_t *p) {
uint8_t mode = p->output
? OUTPUT : INPUT;
if (!p->output && p->pull_up)
mode = INPUT_PULLUP;
pinMode(p->pin, mode);
}
void gpio_pin_set(GpioPin_t *p,
bool state) {
bool level = p->active_high
? state : !state;
digitalWrite(p->pin, level);
}
bool gpio_pin_read(GpioPin_t *p) {
bool raw = digitalRead(p->pin);
return p->active_high ? raw : !raw;
}

## Slide 8
Using the GPIO Driver in main.cpp
#include "gpio_driver.h"
// Declare pins as structs — no "magic numbers" scattered in code
static GpioPin_t led = { .pin = 8, .output = true, .active_high = true, .pull_up = false };
static GpioPin_t button = { .pin = 9, .output = false, .active_high = false, .pull_up = true };
void setup() {
gpio_pin_init(&led);
gpio_pin_init(&button);
}
void loop() {
bool pressed = gpio_pin_read(&button); // abstraction hides active-low detail
gpio_pin_set(&led, pressed); // LED mirrors button state
delay(10);
}
01
Designated initializers (.pin = 8) make struct init readable and safe — no positional mistakes.
02
The driver hides hardware details (active-low, pull-up) behind a clean API.
03
Adding a new pin requires zero code changes — just a new GpioPin_t instance.

## Slide 9
typedef struct — Clean Naming Convention
// Without typedef — verbose
struct GpioPin {
uint8_t pin;
bool output;
};
struct GpioPin led; // need 'struct' keyword
void init(struct GpioPin *p); // everywhere
// With typedef — clean (C99+)
typedef struct {
uint8_t pin;
bool output;
} GpioPin_t;
GpioPin_t led; // no 'struct' keyword
void init(GpioPin_t *p); // cleaner everywhere
Convention: append _t to typedef names (GpioPin_t, SpiConfig_t). Matches stdint.h style (uint8_t, int32_t) — consistent and instantly recognizable as a type.
Avoid typedef for pointer types (e.g. typedef GpioPin_t* PGpioPin).
Hiding the pointer makes code harder to reason about — always write GpioPin_t* p explicitly.

## Slide 10
Arrays of Structs — Managing Multiple Peripherals
// Multiple LEDs — array of structs
static GpioPin_t leds[] = {
{ .pin = 8, .output = true, .active_high = true, .pull_up = false },
{ .pin = 9, .output = true, .active_high = false, .pull_up = false }, // active-low
{ .pin = 10, .output = true, .active_high = true, .pull_up = false },
};
static const uint8_t NUM_LEDS = sizeof(leds) / sizeof(leds[0]);
void setup() {
for (uint8_t i = 0; i < NUM_LEDS; i++) {
gpio_pin_init(&leds[i]); // pointer to each element
}
}
void all_leds_on(void) {
GpioPin_t *p = leds; // pointer arithmetic on array
for (uint8_t i = 0; i < NUM_LEDS; i++, p++) {
gpio_pin_set(p, true);
}
}
leds[i] is equivalent to *(leds + i) — the array name is a pointer to its first element.

## Slide 11
Hands-On Exercise
Build a Button Driver Using a Struct
1
Define a Button_t struct with fields: pin (uint8_t), active_high (bool), debounce_ms (uint16_t), last_state (bool), last_time (uint32_t).
2
Write button_init(Button_t *b) that sets up the pin with INPUT_PULLUP when active_high is false.
3
Write button_read(Button_t *b) that returns a debounced bool using millis() and the struct's last_state / last_time fields.
4
In main.cpp, create one Button_t instance and one GpioPin_t LED. Toggle the LED on each confirmed button press.
BONUS
Create an array of 2 buttons. Print which button was pressed to Serial.

## Slide 12
Summary
struct
Groups heterogeneous data into a single named type. Use typedef struct { } Name_t; convention.
Memory
Compiler adds padding for alignment. sizeof() reveals actual size. Use static_assert to catch surprises.
->
The arrow operator accesses members through a pointer. p->x is (*p).x — always prefer ->.
By pointer
Always pass structs to functions by pointer. Avoids copying, enables mutation, matches driver APIs.
Embedded
Structs are the foundation of C driver design — GPIO, SPI, I2C, UART configs all use this pattern.
Next: Dynamic memory (malloc / free) and linked lists in embedded C