## Slide 1
LESSON 13 | MODULE 4: STM32 PLATFORM
USART3 and I2C1
on NUCLEO-F334R8
CubeMX Peripheral Configuration + OPT4001 Light Sensor
Fundamentals of C++ for Microcontrollers | 2026

## Slide 2
Agenda
1
F334R8 vs F401RE
Key differences: flash, RAM, HRTIM, DAC
2
CubeMX: Clock Setup
HSI PLL -> 64 MHz SYSCLK
3
Adding USART3
PC10/PC11, AF7, Morpho CN7 (flying wires)
4
I2C Protocol + Pull-ups
Open-drain bus, pull-up resistor value selection
5
Adding I2C1
PB6 (SCL) / PB7 (SDA), AF4, Arduino D15/D14
6
OPT4001 Light Sensor
SOT-5X3 variant, address selection, wiring
7
Demo Code + VSCode Setup
HAL_I2C_IsDeviceReady, printf over USART2

## Slide 3
F334R8 vs F401RE: What Changed?
Feature | F401RE | F334R8
Core | Cortex-M4 @ 84 MHz | Cortex-M4 @ 72 MHz
Flash | 512 KB | 64 KB
RAM | 96 KB | 12 KB
Special timer | None | HRTIM (1.25 ns resolution, for power electronics)
DAC | None | 2x 12-bit DAC
USART/UART | USART1/2/6 | USART1/2/3 + UART4/5
I2C | I2C1/2/3 | I2C1/2
LD2 / B1 | PA5 / PC13 | PA5 / PC13 (identical)

## Slide 4
CubeMX: Create New Project for F334R8
1
Open STM32CubeMX or CubeIDE
File > New STM32 Project
2
Board Selector tab
Search: NUCLEO-F334R8, press Enter to confirm
3
Initialize all peripherals
Click Yes -- LD2 (PA5) and B1 (PC13) assigned automatically
4
Verify pinout
Green pins: PA5, PC13. Same positions as F401RE.
5
Set toolchain (Project Manager)
CubeIDE for demo; students: STM32 VS Code Extension
HSI vs HSE on F334R8
The F334R8 has no external crystal fitted on the Nucleo board by default. The main clock source is HSI (8 MHz internal RC oscillator).
The PLL is used to reach 64 MHz (the chip maximum). You will configure this in the Clock Configuration tab.
HSE remains disabled unless you solder a crystal to X3.

## Slide 5
Clock Tree: 64 MHz from HSI PLL
HSI
8 MHz
RC osc
HSI/2
4 MHz
(fixed prediv)
PLL
x16
64 MHz
SYSCLK
64 MHz
(max)
AHB
HPRE /1
64 MHz
APB1/2
PPRE /1
64 MHz
CubeMX Steps
1. Pinout & Configuration > System Core > RCC: HSE = Disabled, HSI = Enabled (default)
2. Switch to Clock Configuration tab. Set PLL Source = HSI/2, PLLMUL = x16
3. Set SYSCLK source = PLLCLK. Result: 64 MHz. AHB and APB prescalers = 1
4. CubeMX highlights out-of-range values in red. No red cells means configuration is valid

## Slide 6
USART2: ST-Link VCP (Preconfigured)
What is the VCP?
The ST-Link debugger on the Nucleo board exposes a Virtual COM Port (VCP) over USB. CubeMX automatically assigns USART2 (PA2 TX / PA3 RX) to this link on F334R8, exactly as on F401RE.
redirecting printf() to USART2 lets you send debug text to a serial terminal on your PC with no extra hardware.
Pin Assignment
Signal | Pin | AF | Direction
TX | PA2 | AF7 | MCU -> ST-Link -> PC
RX | PA3 | AF7 | PC -> ST-Link -> MCU
Retargeting printf()
/* main.c USER CODE BEGIN 0 */
#include <stdio.h>
int __io_putchar(int ch) {
HAL_UART_Transmit(
&huart2,
(uint8_t *)&ch,
1,
HAL_MAX_DELAY
);
return ch;
}
/* USER CODE END 0 */
USART2 baud rate: 115200
Set in CubeMX > Connectivity > USART2 > Parameter Settings

## Slide 7
Adding USART3: PC10 / PC11 (Morpho CN7)
CubeMX Configuration
1
Connectivity > USART3
Set Mode to Asynchronous
2
Parameter Settings
Baud Rate: 115200, 8N1 (8 bits, no parity, 1 stop bit)
3
CubeMX auto-assigns pins
PC10 = USART3_TX (AF7), PC11 = USART3_RX (AF7)
4
Pins turn green in pinout view
Verify in the chip diagram on the left
Signal | Pin | AF | Connector
TX | PC10 | AF7 | Morpho CN7
RX | PC11 | AF7 | Morpho CN7
Morpho CN7 (left header)
CN7 Pin | Signal
1 | PC10 / USART3_TX
2 | PC11 / USART3_RX
GND pin | GND -- also connect this
Flying wires to a USB-UART adapter:
TX (PC10) -> RX on adapter
RX (PC11) -> TX on adapter
GND -> GND on adapter
The F334R8 I/O is 3.3 V. Do NOT connect to a 5 V UART adapter without a level shifter.
Verify the exact CN7 row in the board silkscreen -- pin 1 is marked with an arrow.

## Slide 8
I2C Protocol Basics
Key Concepts
Two-wire bus
SCL carries the clock; SDA carries data. Both lines are pulled high by external resistors.
Open-drain
Devices can only pull a line LOW by activating an N-channel FET. They release the line to let the pull-up restore it HIGH. No device ever drives HIGH actively.
7-bit address
Each target device has a unique 7-bit address. The master sends ADDR[6:0] followed by a direction bit: 0 = write, 1 = read.
ACK / NACK
After each byte the receiver pulls SDA low for one clock (ACK). If SDA stays high it is a NACK. A missing ACK means the address was not recognized.
Transactions
A complete read: START, ADDR+W, REG, STOP/RESTART, ADDR+R, DATA bytes, NACK, STOP.
I2C Write Transaction
START
|
+-- [ADDR 0x44] [W=0] <- master sends
| [ACK] <- sensor pulls SDA low
|
+-- [REG ADDR 0x0A] <- register pointer
| [ACK]
|
RESTART
|
+-- [ADDR 0x44] [R=1] <- master sends
| [ACK] <- sensor ACKs
|
+-- [DATA byte 0] <- sensor sends
| [ACK by master]
+-- [DATA byte 1]
| [NACK by master] <- signals last byte
|
STOP

## Slide 9
I2C Pull-up Resistors
Why are pull-ups required?
I2C lines are open-drain. No device drives them HIGH. The pull-up resistor (Rp) connected between the line and VDD is the only source that restores a line to logic HIGH when the bus is idle or released.
Without pull-ups both SCL and SDA float. The I2C peripheral will never see valid logic levels and the bus will not function.
Value Selection
Speed Mode | Typical Rp | When to use
Standard 100 kHz | 10 kOhm | Long wires, many devices on bus
Fast 400 kHz | 4.7 kOhm | Most sensor applications
Fast-plus 1 MHz | 2.2 kOhm | Short PCB traces only
Circuit
VDD (3.3 V)
| |
Rp Rp
4.7k 4.7k
| |
---+-- SCL +-- SDA ---
| |
[F334R8 I2C1] [OPT4001]
| |
GND GND
The OPT4001 eval board already has 10 kOhm pull-ups installed. For 400 kHz you can add 4.7 kOhm resistors in parallel (result: ~3.2 kOhm). No extra resistors needed for 100 kHz (standard mode).

## Slide 10
Adding I2C1: PB6 (SCL) / PB7 (SDA)
CubeMX Configuration
1
Connectivity > I2C1
Set I2C mode to I2C
2
Parameter Settings
Speed Mode: Fast Mode, Speed Frequency: 400000 Hz
3
Pin assignment (automatic)
PB6 = I2C1_SCL (AF4), PB7 = I2C1_SDA (AF4)
4
Arduino connector location
PB6 = D15 (top of CN5), PB7 = D14 (second from top)
5
GPIO mode (set by CubeMX)
Alternate Function Open Drain, Pull-up, Very High Speed
I2C1 Pin Summary
Signal | Pin | AF | Arduino
SCL | PB6 | AF4 | D15 (CN5)
SDA | PB7 | AF4 | D14 (CN5)
GPIO Configuration Detail
Mode: Alternate Function Open Drain
Pull-up/Pull-down: Pull-up
Maximum speed: Very High
Alternate Function: AF4 (I2C1_SCL / I2C1_SDA)
Open Drain is required by the I2C
specification. Never change it to
Push-Pull -- this will fight the
pull-up resistors on the bus.

## Slide 11
CubeMX: Generate the Project
Project Manager Tab
1
Project Name
lesson13_i2c_uart
2
Toolchain / IDE
CubeIDE (demo) or STM32 VS Code Extension (students)
3
Code Generator
Select: Copy only the necessary library files
4
Generate Code
Alt+K or button. CubeMX opens the project folder.
Generated Project Structure
Generated File Structure
lesson13_i2c_uart/
Core/
Inc/
main.h <- peripheral handles
Src/
main.c <- your code lives here
stm32f3xx_it.c
Drivers/
STM32F3xx_HAL_Driver/
CMSIS/
lesson13.ioc <- CubeMX project file
Generated handles (main.c)
UART_HandleTypeDef huart2; /* VCP */
UART_HandleTypeDef huart3; /* ext */
I2C_HandleTypeDef hi2c1; /* sensor*/
/* USER CODE BEGIN 0 */
/* USER CODE END 0 */
Always write your code between USER CODE BEGIN and END comments. CubeMX preserves these blocks when you regenerate.

## Slide 12
OPT4001: High-Precision Ambient Light Sensor
Key Specifications (SOT-5X3 Package)
Type
Single-chip lux meter. Spectral response matches the human eye.
Dynamic range
437.5 uLux to 117 kLux (28-bit effective, SOT-5X3 variant)
Gain ranges
9 logarithmic ranges with automatic selection. No manual gain programming needed.
I2C speed
Standard 100 kHz, Fast 400 kHz, High-Speed 2.6 MHz
Supply
1.6 V to 3.6 V. I/O tolerant up to 5.5 V. Safe with 3.3 V Nucleo.
Current
30 uA active, 2 uA standby
I2C Address (SOT-5X3 ADDR Pin)
ADDR pin | 7-bit address
GND | 0x44
VDD | 0x45
SDA | 0x46
SCL | 0x47
Eval board default:
ADDR pin tied to GND --> address 0x44.
Verify on your board: check the silkscreen or schematic for the ADDR solder bridge / jumper position.

## Slide 13
Wiring the OPT4001 Eval Board to Nucleo
OPT4001 Pin | Nucleo Pin | Header | Notes
VDD | 3V3 | CN6 pin 4 | 3.3 V supply to sensor
GND | GND | CN6 pin 6 | Common ground -- required
SCL | PB6 | D15 (CN5) | I2C1 clock, AF4, open-drain
SDA | PB7 | D14 (CN5) | I2C1 data, AF4, open-drain
ADDR | GND | CN6 pin 6 | Selects I2C address 0x44
INT | (NC) | -- | Interrupt -- not used in this lesson
IMPORTANT: The eval board has 10 kOhm pull-ups on SCL and SDA already. No extra resistors are needed for 100 kHz operation. For 400 kHz add 4.7 kOhm in parallel. The sensor I/O is 5.5 V tolerant but power it from 3.3 V only.
Connect GND between Nucleo and eval board. Floating ground = no communication. Check with a multimeter before powering on.

## Slide 14
Using the ST-Link Debugger
CubeIDE (demo)
Debug button
Click the bug icon (not the arrow). CubeIDE flashes and halts at main().
F8
Continue -- run until next breakpoint
F6
Step over -- execute current line, stay in function
F5
Step into -- follow a function call inside
Breakpoint
Click the line number margin. Red dot appears. Execution stops there.
Variables view
Left panel -- shows all local and global variables live
Expressions
Window > Show View > Expressions. Type any variable or address to watch it.
Registers
Window > Show View > Registers. Shows raw CPU and peripheral registers.
VS Code Extension
F5
Start debugging
F6
Step over
F11
Step into
Shift+F5
Stop session
Breakpoint
Click line number margin -- same as CubeIDE
Watch
Run > Add Watch -- type variable name
Lesson 13 tip
Set a breakpoint after HAL_I2C_IsDeviceReady() and hover over result:
result == 0 -> HAL_OK
result == 1 -> HAL_ERROR
No printf needed. The debugger shows the value live -- this is the point of a hardware debugger.
How it works:
The ST-Link chip on the Nucleo board connects to the STM32 over SWD (SWDCLK + SWDIO, 2 wires). One USB cable does everything: power, flash, and full hardware debug. Breakpoints, single-stepping, variable inspection, and register reads all work without any printf or logic analyzer.

## Slide 15
HAL I2C API Essentials
HAL_I2C_IsDeviceReady()
Probe the bus. Sends address, checks for ACK. Returns HAL_OK if the device responded.
HAL_StatusTypeDef ret =
HAL_I2C_IsDeviceReady(
&hi2c1, /* handle */
0x44 << 1, /* 8-bit address */
3, /* retries */
100 /* timeout ms */
);
HAL_I2C_Master_Transmit()
Write bytes to the target (e.g. set a register pointer or write config).
uint8_t reg = 0x0A;
HAL_I2C_Master_Transmit(
&hi2c1, 0x44 << 1,
&reg, 1, HAL_MAX_DELAY);
HAL_I2C_Master_Receive()
Read bytes from the target after pointing to a register.
uint8_t buf[2];
HAL_I2C_Master_Receive(
&hi2c1, (0x44 << 1) | 0x01,
buf, 2, HAL_MAX_DELAY);
Address note: HAL_I2C_IsDeviceReady handles the shift internally. For Transmit/Receive you must pass the 8-bit address: write = addr << 1, read = (addr << 1) | 0x01.

## Slide 16
Demo: Ping OPT4001, Report over USART2
/* USER CODE BEGIN 0 */
#include <stdio.h>
#define OPT4001_ADDR (0x44 << 1)
int __io_putchar(int ch) {
HAL_UART_Transmit(&huart2,
(uint8_t *)&ch, 1, HAL_MAX_DELAY);
return ch;
}
/* USER CODE END 0 */
/* USER CODE BEGIN WHILE */
while (1) {
HAL_StatusTypeDef ret;
ret = HAL_I2C_IsDeviceReady(
&hi2c1, OPT4001_ADDR, 3, 100);
if (ret == HAL_OK) {
printf("OPT4001 found at 0x44\r\n");
HAL_GPIO_TogglePin(LD2_GPIO_Port,
LD2_Pin);
} else {
printf("No ACK -- check wiring\r\n");
}
HAL_Delay(1000);
}
/* USER CODE END WHILE */
What to Observe
Serial terminal
Open at 115200 on ST-Link VCP. Should print 'OPT4001 found at 0x44' once per second.
Logic analyzer
Probe PB6 (SCL) and PB7 (SDA). Observe START, address byte 0x88, ACK pulled low by sensor.
LD2 heartbeat
The green LED toggles on each successful ACK -- a quick visual sanity check.
NACK scenario
Disconnect SDA. Terminal shows 'No ACK'. IsDeviceReady retries 3 times, then returns HAL_ERROR.

## Slide 17
STM32 VS Code Extension: Open the Project
1
Install the extension
Search 'STM32 VS Code Extension' in the Marketplace. Publisher: ST Microelectronics.
2
Open project folder
File > Open Folder > select the CubeMX-generated project root (contains .ioc file)
3
Build
Click Build in the STM32 sidebar, or Ctrl+Shift+B. Output goes to the build/ folder.
4
Flash and debug
Connect Nucleo via USB. Press F5 or Run > Start Debugging. ST-Link is used automatically.
5
Serial monitor
Any terminal at 115200 on the ST-Link VCP COM port (Windows: COMx, Linux: /dev/ttyACMx).
6
Reconfigure peripherals
Edit the .ioc file in CubeMX, click Generate Code. The VS Code project updates in place.
7
Protect user code
Only write code between USER CODE BEGIN / END blocks. CubeMX never touches those sections.
8
Workspace tip
Keep the .ioc file in version control. It is the source of truth for peripheral configuration.