## Slide 1
LESSON 06
Classes, Objects
and Encapsulation
From C structs to C++ classes
Embedded Systems Course 2026 | ESP32-C3 Super Mini

## Slide 2
Today's Agenda
From Structs to Classes
Why C++ classes exist and how they differ from C structs
Encapsulation
public, private, protected — hiding implementation details
Constructors & Destructors
Object lifecycle — init and cleanup done right
Methods & this Pointer
Member functions, const correctness, operator overloads
Practical: Rewriting Drivers
GpioPin and Button as C++ classes on ESP32-C3

## Slide 3
From Structs to Classes
C Approach (Lesson 4)
typedef struct {
uint8_t pin;
bool active_high;
} GpioPin_t;
void gpio_pin_init(GpioPin_t *p);
void gpio_pin_set(GpioPin_t *p,
bool state);
bool gpio_pin_read(GpioPin_t *p);
C++ Approach (Today)
class GpioPin {
private:
uint8_t pin_;
bool active_high_;
public:
GpioPin(uint8_t pin, bool ah);
void set(bool state);
bool read() const;
};
Data + functions that operate on that data = bundled together in one unit

## Slide 4
Anatomy of a C++ Class
class Led { // class keyword + name
private: // --- hidden from outside ---
uint8_t pin_; // data members (fields)
bool active_high_;
bool state_;
public: // --- accessible from outside ---
Led(uint8_t pin, bool ah); // constructor
~Led(); // destructor
void on(); // member functions (methods)
void off();
void toggle();
bool isOn() const; // const = does not modify object
}; // <-- semicolon required!
private
section
public
section

## Slide 5
Access Specifiers
public
Anyone can access.
This is your API — the interface
other code uses.
private
Only the class itself can access.
Hide implementation details.
Default in class.
protected
Class + its children can access.
Used with inheritance.
(Lesson 7)
class vs struct in C++: The only difference is the default access. struct = public by default. class = private by default.

## Slide 6
Why Encapsulation Matters
Without encapsulation
Led myLed;
myLed.pin_ = 8;
myLed.state_ = true;
// Oops — forgot to call pinMode!
// Hardware is now in unknown state
With encapsulation
Led myLed(8, true); // constructor
myLed.on(); // clean API
myLed.toggle();
// Cannot touch pin_ or state_
// Hardware always consistent
Benefits for embedded systems:
Hardware is always in a valid state — constructor guarantees proper init
API is clear — users see only what they need (on/off/toggle/read)
Internal changes do not break user code — swap GPIO lib, API stays the same
Bugs are localized — if state_ is wrong, the bug is inside the class

## Slide 7
Constructors
A constructor runs automatically when an object is created
// In the header (Led.h)
class Led {
private:
uint8_t pin_;
bool active_high_;
bool state_;
public:
Led(uint8_t pin, bool active_high); // declaration
};
// In the source (Led.cpp)
Led::Led(uint8_t pin, bool active_high) // definition
: pin_(pin) // initializer list
, active_high_(active_high)
, state_(false)
{
pinMode(pin_, OUTPUT); // hardware init
set(false); // start OFF
}
Same name as the class, no return type
Initializer list: preferred over assignment in body

## Slide 8
Destructors & Object Lifetime
class Led {
public:
Led(uint8_t pin, bool ah);
~Led(); // destructor: ~ClassName
};
Led::~Led() {
set(false); // turn off LED on destroy
}
Object lifetime on the stack:
void doWork() {
Led led(8, true); // constructor called here — LED initialized
led.on(); // use the object
} // destructor called here — LED turned off
In embedded systems
Most objects live forever
(global or static scope).
Destructors rarely run
in typical firmware.
Still important to
understand the concept
for RAII (Lesson 8).

## Slide 9
The this Pointer
Every member function receives a hidden pointer to the object it was called on
void Led::on() {
this->state_ = true; // explicit this->
state_ = true; // same thing — this-> is implicit
digitalWrite(this->pin_,
active_high_ ? HIGH : LOW);
}
Remember the C version?
// C: you pass the pointer yourself
void gpio_pin_set(GpioPin_t *p,
bool state);
C++ does the same thing — it just hides the pointer for you!

## Slide 10
Methods & const Correctness
class Led {
public:
void on(); // modifies state_ -> non-const
void off(); // modifies state_ -> non-const
void toggle(); // modifies state_ -> non-const
bool isOn() const; // read-only -> mark const
uint8_t pin() const; // read-only -> mark const
};
// const method implementation:
bool Led::isOn() const {
return state_; // OK: reading is fine
// state_ = true; // ERROR: cannot modify in const method
}
Rule of thumb: If a method does not modify the object, mark it const. This catches bugs at compile time and allows use with const references.

## Slide 11
Header and Source Files
Led.h
#pragma once
#include <stdint.h>
class Led {
private:
uint8_t pin_;
bool active_high_;
bool state_;
public:
Led(uint8_t pin, bool ah);
~Led();
void on();
void off();
void toggle();
bool isOn() const;
};
Led.cpp
#include "Led.h"
#include <Arduino.h>
Led::Led(uint8_t pin, bool ah)
: pin_(pin)
, active_high_(ah)
, state_(false)
{
pinMode(pin_, OUTPUT);
off();
}
Led::~Led() { off(); }
void Led::on() {
state_ = true;
uint8_t level = active_high_
? HIGH : LOW;
digitalWrite(pin_, level);
}
#pragma once = include guard. Led::on() = scope resolution operator :: tells compiler which class the method belongs to.

## Slide 12
Practical: GpioPin Class
class GpioPin {
private:
uint8_t pin_;
bool output_; // true = output, false = input
bool active_high_;
bool pull_up_;
public:
GpioPin(uint8_t pin, bool output, bool active_high,
bool pull_up = false);
void set(bool state);
void toggle();
bool read() const;
uint8_t pin() const { return pin_; } // inline getter
};
// Usage on ESP32-C3:
GpioPin onboardLed(8, true, true); // output, active-high
GpioPin button(0, false, false, true); // input, active-low, pull-up
void setup() {
onboardLed.set(true); // LED on
}

## Slide 13
Practical: Button Class
class Button {
private:
uint8_t pin_;
bool active_high_;
uint16_t debounce_ms_;
// Internal state
bool last_raw_;
bool stable_state_;
uint32_t last_change_;
bool event_pending_;
public:
Button(uint8_t pin, bool active_high,
uint16_t debounce_ms = 50);
void update(); // call every loop iteration
bool pressed(); // true once per press event
bool state() const; // current stable state
};
// Usage:
Button btn(0, false, 50); // GPIO 0, active-low, 50ms debounce
void loop() {
if (btn.pressed()) {
Serial.println("Click!");
}
}

## Slide 14
C++ on Microcontrollers
What costs nothing (zero overhead)
Classes and encapsulation
Constructors / destructors
References (T&)
Namespaces
const / constexpr
enum class (scoped enums)
What to be careful with
new / delete (heap fragmentation)
Exceptions (-fno-exceptions)
RTTI (-fno-rtti)
Virtual functions (vtable cost)
STL containers (std::vector, etc.)
std::string (dynamic allocation)
The ESP32 has enough RAM (320 KB) and runs at 160 MHz.
You can use more C++ features than on an 8-bit AVR (2 KB RAM).
But good habits matter — write code that works on any MCU, not just ESP32.

## Slide 15
Default Parameters & Overloading
Default parameter values
class Button {
public:
Button(uint8_t pin,
bool ah = false,
uint16_t db = 50);
};
Button b1(0); // ah=false, db=50
Button b2(0, true); // db=50
Button b3(0, true, 80); // all explicit
Constructor overloading
class Led {
public:
Led(uint8_t pin);
Led(uint8_t pin, bool ah);
};
// Compiler picks the right one:
Led red(8); // 1-arg ctor
Led green(3, false); // 2-arg ctor
Getters and Setters — the C++ way
class Led {
private:
uint8_t pin_;
public:
uint8_t pin() const { return pin_; } // getter — inline in header
// No setter for pin_ — it should never change after construction!
};

## Slide 16
Practice Exercises
1
Exercise 1 — Read the template
Open the project. Read Led.h, Led.cpp, Button.h, Button.cpp.
Flash the code. Verify LED blinks and button prints to Serial.
2
Exercise 2 — Add a method
Add a blink(uint16_t ms) method to the Led class.
It should turn the LED on, wait ms milliseconds, then turn off.
3
Exercise 3 — Create an RgbLed class
Create a new class RgbLed that holds three GpioPin objects
(red, green, blue). Add methods: setColor(r, g, b) and off().
4
BONUS — Cycle colors with Button
Use your RgbLed + Button to cycle through
Red -> Green -> Blue -> White -> Off on each press.

## Slide 17
Homework 6
Traffic Light Controller
Create a TrafficLight class that controls 3 LEDs (R, G, B channels of your RGB LED)
Implement states: RED, YELLOW (R+G), GREEN, and transition logic
Add a Button input: each press advances to the next state
The class must use encapsulation: all state data is private
Provide a clean public API: next(), currentState(), begin()
Print state transitions to Serial
Use header + source file split (TrafficLight.h / TrafficLight.cpp)
Due: before Lesson 7 | Push to your GitHub repository

## Slide 18
Summary
class bundles data + functions together (struct with methods)
private hides internals, public defines the API
Constructor initializes the object (replaces init functions)
Destructor cleans up (important for RAII in Lesson 8)
const methods promise not to modify the object
C++ classes have zero overhead vs C structs + functions
Next: Lesson 07
Inheritance, Templates, Data Structures
Base classes, virtual functions, generic programming with templates, ring buffers