## Slide 1
MODULE 2 // C++ FUNDAMENTALS
RAII, Memory Handling,
Standard Libraries
Lesson 8
Embedded Systems Course 2026 | ESP32-C3 Super Mini

## Slide 2
Today's Agenda
RAII
Automatic resource
management via
constructor / destructor
Memory Handling
Stack vs Heap,
new/delete pitfalls,
placement new
Standard Libraries
What parts of STL
are usable on ESP32
with Arduino

## Slide 3
The Problem: Unmanaged Resources
What can go wrong?
void blinkTask() {
pinMode(LED_PIN, OUTPUT);
// ... some logic ...
if (error) return;
// early return!
digitalWrite(LED_PIN, LOW);
}
Consequences
GPIO left in unknown state
LED stays ON after error
Buffer not freed on exception path
Timer keeps running after task ends
No cleanup on early return

## Slide 4
RAII: Resource Acquisition Is Initialization
Constructor
Acquires the resource:
pinMode(), allocate buffer,
start timer, open file
Destructor
Releases the resource:
digitalWrite(LOW), free buffer,
stop timer, close file
Key Insight
The compiler guarantees the destructor runs when the object goes out of scope.
Even on early return, even on exception. Cleanup is automatic and unavoidable.
Lesson 8 | RAII, Memory Handling, Standard Libraries

## Slide 5
RAII in Practice: PinOwner
class PinOwner {
uint8_t pin_;
bool state_;
public:
PinOwner(uint8_t p, uint8_t mode)
: pin_(p), state_(false) {
pinMode(pin_, mode);
}
~PinOwner() {
digitalWrite(pin_, LOW);
pinMode(pin_, INPUT);
}
void set(bool v) {
state_ = v;
digitalWrite(pin_, v);
}
};
Constructor configures
the pin (acquires resource)
Destructor resets pin
to safe INPUT state
Object goes out of scope?
Destructor runs
automatically!

## Slide 6
Scope-Based Lifetime
void doWork() {
PinOwner led(3, OUTPUT);
// ^ constructor runs here
led.set(HIGH);
delay(1000);
if (checkError()) return;
// ^ destructor STILL runs!
led.set(LOW);
} // destructor runs here too
Object created
Resource in use
Early return?
Destructor runs

## Slide 7
Memory Layout: Stack vs Heap
STACK
Automatic storage (local vars)
Fixed size (~8 KB per task on ESP32)
LIFO: grows/shrinks with scope
Very fast allocation (pointer bump)
No fragmentation
Compiler manages lifetime
HEAP
Dynamic storage (new / malloc)
Shared pool (~300 KB on ESP32-C3)
Allocated / freed in any order
Slower: allocator overhead
Fragmentation over time!
YOU manage lifetime
Lesson 8 | RAII, Memory Handling, Standard Libraries

## Slide 8
ESP32-C3 Memory Map
~400 KB SRAM total, but your app gets much less
Flash (4 MB)
Code, .rodata, string literals
.data + .bss
Globals, static variables
Heap (~300 KB)
malloc / new / Arduino String internals
Task Stacks (in Heap!)
loop() = 8 KB, each xTaskCreate gets its own
IDF + Wi-Fi/BLE
Reserved by ESP-IDF runtime
FreeRTOS Key Fact
Task stacks are allocated FROM the heap!
No classic "stack grows down, heap grows up" model. Each task gets a fixed-size block carved out of the shared heap pool.
int x = 5;
Stack
static int count;
.bss
new PinOwner(...)
Heap
"hello"
Flash

## Slide 9
Stack Overflow: How It Happens
Unbounded Recursion
void boom(uint32_t depth) {
uint8_t pad[128]; // 128 B/frame
Serial.printf(
"depth: %u\n", depth);
boom(depth + 1);
// never returns!
}
void setup() { boom(0); }
Large Local Array
void setup() {
// 16 KB > 8 KB stack!
uint8_t big[16384];
memset(big, 0,
sizeof(big));
}
ESP32 Response:
Stack canary watchpoint triggered (loopTask)
8192 bytes / ~160 bytes per frame = ~51 calls before crash. With pad[128], even fewer.
Lesson 8 | RAII, Memory Handling, Standard Libraries

## Slide 10
Runtime Stack & Heap Monitoring
void printDiagnostics() {
UBaseType_t hwm =
uxTaskGetStackHighWaterMark(NULL);
size_t freeHeap =
heap_caps_get_free_size(MALLOC_CAP_DEFAULT);
size_t maxBlock =
heap_caps_get_largest_free_block(
MALLOC_CAP_DEFAULT);
Serial.printf("HWM:%u H:%u B:%u\n",
hwm, freeHeap, maxBlock);
}
HighWaterMark
Minimum free stack EVER.
Approaching 0 = danger!
free_size
Total free heap bytes.
Declining over time = leak.
largest_free_block
Biggest contiguous block.
Small vs free_size = fragmentation!
Call printDiagnostics() periodically in loop() during development. Remove for production.

## Slide 11
Why Avoid new/delete on MCU?
Heap over time:
T1: Fresh
T2: After free()
T3: Need 3 blocks
4 free blocks, but not contiguous. Allocation of 3 fails!
No MMU
MCUs have no Memory Management Unit. No virtual memory, no page swapping.
Fragmented heap = permanent problem until reboot. Long-running systems eventually crash.

## Slide 12
Checking Heap at Runtime
#include <esp_heap_caps.h>
void printHeapInfo() {
Serial.printf("Free heap: %u bytes\n",
heap_caps_get_free_size(MALLOC_CAP_DEFAULT));
Serial.printf("Largest block: %u bytes\n",
heap_caps_get_largest_free_block(
MALLOC_CAP_DEFAULT));
}
Tip: Compare free_size vs largest_block. Big gap = fragmentation!

## Slide 13
Placement new & Static Pools
Pre-allocate memory at compile time. Construct objects in-place at runtime.
#include <new> // for placement new
// Static buffer - no heap!
alignas(PinOwner)
uint8_t buf[sizeof(PinOwner)];
// Construct in pre-allocated buf
auto* p = new (buf) PinOwner(3, OUTPUT);
// Must manually call destructor
p->~PinOwner();
When to use:
Object pools for sensors
Fixed-size buffer arrays
ISR-safe data structures
Zero heap allocation systems
Lesson 8 | RAII, Memory Handling, Standard Libraries

## Slide 14
C++ Standard Libraries on ESP32
Header | Status | Notes
<array> | Safe | Fixed-size, stack-allocated, no overhead
<algorithm> | Safe | sort, find, min, max, clamp — all useful
<cstring> | Safe | memcpy, memset, strlen — C classics
<cstdint> | Safe | uint8_t, int32_t — already using these!
<type_traits> | Safe | Compile-time checks, zero runtime cost
<string> | Caution | Dynamic allocation — heap fragmentation risk
<vector> | Caution | Grows dynamically — same risk as string
<iostream> | Avoid | Huge binary size, use Serial instead

## Slide 15
Strings on MCU: Three Approaches
char[]
No heap allocation
Predictable memory
Fast, no overhead
Manual buffer mgmt
Recommended
std::string
Convenient API
Dynamic allocation
Heap fragmentation
Hidden copies
Use with care
Arduino String
Easy concatenation
Heavy heap usage
Worst fragmentation
Reallocates often
Avoid if possible

## Slide 16
RAII + Memory: The Pattern
Static
Allocation
compile-time
Constructor
Initializes
acquires resource
Object
In Use
scope-bound
Destructor
Cleans Up
automatic
Prefer stack allocation over heap
Use RAII to tie resource lifetime to object lifetime
If you must use heap, wrap it in an RAII class
Monitor heap with heap_caps_ functions during development
Lesson 8 | RAII, Memory Handling, Standard Libraries

## Slide 17
Summary
RAII
Constructor acquires, destructor releases. Compiler guarantees cleanup on scope exit.
Stack over Heap
Stack is fast and predictable. Heap fragments without MMU. Avoid new/delete when possible.
Placement new
Pre-allocate static buffers. Construct objects in-place. Zero heap overhead.
STL on ESP32
<array>, <algorithm>, <cstring> are safe. Avoid <iostream>, be careful with <string> and <vector>.
Lesson 8 | RAII, Memory Handling, Standard Libraries

## Slide 18
What's Next?
Homework assignment (TBD)
Practice RAII with PinOwner or similar classes
Experiment with heap monitoring via Serial
Refactor previous lesson code using RAII principles
Embedded Systems Course 2026 | ESP32-C3 Super Mini