## Slide 1
LESSON 11
em_color & Joystick
Color abstraction + analog input in the drivers library
common::
drivers::
ESP32-C3
Fundamentals of C++ for Microcontrollers | 2026

## Slide 2
Lesson 11 — Agenda
What we cover today
1
em_color struct
A reusable color type in namespace common
2
Named color constants
RED, GREEN, BLUE, WHITE, BLACK, YELLOW, CYAN, MAGENTA
3
Color lerp()
Linear interpolation between two colors
4
RgbLed update
setColor(const common::em_color&) added to existing class
5
Joystick hardware
Two potentiometers + push button on ESP32-C3 ADC
6
Joystick class
Composition: AnalogPin x2 + Button, mapped -100..+100, dead zone
7
Demo + Homework
Joystick controls RGB LED color via em_color lerp

## Slide 3
Why a Color Type?
The problem with raw bytes
Without em_color
// Caller must know the order!
led.setColor(255, 0, 0);
// What does this mean?
led.setColor(0, 100, 200);
// Easy to mix up R/G/B
uint8_t r = 0, g = 255, b = 0;
led.setColor(b, r, g); // BUG
With em_color
using namespace common;
// Clear and self-documenting
led.setColor(em_color::RED);
// Explicit construction
em_color sky(135, 206, 235);
led.setColor(sky);
// Reusable, composable
led.setColor(lerp(RED, BLUE, t));

## Slide 4
em_color — Struct Layout
namespace common | include/color.h
// include/color.h
#pragma once
#include <stdint.h>
namespace common {
struct em_color {
uint8_t r;
uint8_t g;
uint8_t b;
em_color();
em_color(uint8_t r, uint8_t g, uint8_t b);
static const em_color RED;
static const em_color GREEN;
static const em_color BLUE;
static const em_color WHITE;
static const em_color BLACK;
static const em_color YELLOW;
static const em_color CYAN;
static const em_color MAGENTA;
};
em_color lerp(em_color a, em_color b, uint8_t t);
} // namespace common
Memory layout (3 bytes)
r
+0
g
+1
b
+2
uint8_t [0..255] each field
Key points:
No float: integer math only, MCU-friendly
sizeof(em_color) == 3 bytes — compact
default constructor sets r=g=b=0 (BLACK)
static consts defined in color.cpp

## Slide 5
Named Color Constants
Defined in color.cpp | used via common::em_color::RED
RED
{255, 0, 0}
GREEN
{ 0,255, 0}
BLUE
{ 0, 0,255}
WHITE
{255,255,255}
BLACK
{ 0, 0, 0}
YELLOW
{255,255, 0}
CYAN
{ 0,255,255}
MAGENTA
{255, 0,255}
Usage:
led.setColor(common::em_color::CYAN); // or: using namespace common; led.setColor(em_color::CYAN);

## Slide 6
Color Interpolation — lerp()
Smooth transition between two colors
em_color lerp(em_color a, em_color b, uint8_t t) // t: 0=full a, 255=full b
t = 0
t = 255
lerp(RED, BLUE, t) as t goes 0 -> 255
Implementation (color.cpp):
em_color lerp(em_color a, em_color b, uint8_t t) {
// Scale to 0-255 range using integer math
uint16_t inv = 255u - t;
uint8_t r = (uint8_t)((a.r * inv + b.r * t) / 255u);
uint8_t g = (uint8_t)((a.g * inv + b.g * t) / 255u);
uint8_t bv = (uint8_t)((a.b * inv + b.b * t) / 255u);
return em_color(r, g, bv);
}
Typical usage:
uint8_t t = 0;
void loop() {
auto c = lerp(
em_color::RED,
em_color::BLUE,
t);
led.setColor(c);
t++; // wraps 255->0
delay(10);
}

## Slide 7
RgbLed — Adding setColor(em_color)
Extending the Lesson 9 class
Before (Lesson 9)
class RgbLed {
public:
RgbLed(uint8_t pin_r,
uint8_t pin_g,
uint8_t pin_b);
void setColor(uint8_t r,
uint8_t g,
uint8_t b);
void off();
private:
PwmPin _r, _g, _b;
};
>
After (Lesson 11)
#include "color.h"
class RgbLed {
public:
RgbLed(uint8_t pin_r,
uint8_t pin_g,
uint8_t pin_b);
void setColor(uint8_t r,
uint8_t g,
uint8_t b);
// NEW:
void setColor(
const common::em_color& c);
void off();
private:
PwmPin _r, _g, _b;
};
Both overloads coexist — old code calling setColor(r, g, b) continues to work without changes.

## Slide 8
Joystick Module — Hardware
Two potentiometers + tactile button
Inside the module:
VRx
Potentiometer — X axis (ADC input)
VRy
Potentiometer — Y axis (ADC input)
SW
Push button (active-low, pull-up)
VCC
3.3 V power supply
GND
Ground
Suggested pin assignment (ESP32-C3):
VRx -> GPIO 4 (ADC1 CH4)
VRy -> GPIO 5 (ADC1 CH5)
SW -> GPIO 6 (digital, pull-up)
ESP32-C3 ADC notes
12-bit ADC: values 0 - 4095
ADC1 pins only (ADC2 conflicts with WiFi)
analogRead() returns uint16_t
Center resting: ~2048 (may drift)
map() used to convert to -100..+100
Dead zone compensates center noise

## Slide 9
Joystick — Class Design
Composition over inheritance
Joystick
namespace drivers
AnalogPin _x
AnalogPin _y
Button _btn
Public API:
Joystick(uint8_t pin_x, uint8_t pin_y,
uint8_t pin_btn, uint8_t dead_zone = 10);
void update(); // call every loop
int8_t getX() const; // -100..+100
int8_t getY() const; // -100..+100
bool isPressed() const; // button state
bool wasPressed(); // edge detect

## Slide 10
Axis Mapping & Dead Zone
From raw ADC to signed int8_t
ADC range 0 - 4095
0
~2048
4095
Mapped -100 .. +100
-100
0 (dead zone)
+100
int8_t Joystick::_mapAxis(uint16_t raw) const {
// map 0-4095 to -100..+100
int16_t v = (int16_t)map(raw, 0, 4095,
-100, 100);
// apply dead zone
if (v > -(int8_t)_dz && v < (int8_t)_dz) {
return 0;
}
return (int8_t)v;
}
void Joystick::update() {
_vx = _mapAxis(_x.read());
_vy = _mapAxis(_y.read());
_btn.update();
}
Dead zone prevents jitter when the joystick is at rest near center. Constructor default: dead_zone = 10 (maps to ~10 units out of 100).

## Slide 11
Joystick — Full Header
include/joystick.h | namespace drivers
#pragma once
#include <stdint.h>
#include "analog_pin.h"
#include "button.h"
namespace drivers {
class Joystick {
public:
Joystick(uint8_t pin_x, uint8_t pin_y,
uint8_t pin_btn,
uint8_t dead_zone = 10);
void update();
int8_t getX() const; // -100..+100
int8_t getY() const; // -100..+100
bool isPressed() const;
bool wasPressed();
private:
AnalogPin _x;
AnalogPin _y;
Button _btn;
uint8_t _dz;
int8_t _vx;
int8_t _vy;
int8_t _mapAxis(uint16_t raw) const;
};
} // namespace drivers

## Slide 12
Demo — Joystick Controls RGB Color
Joystick X axis -> lerp RED to BLUE, button -> WHITE flash
demo/src/main.cpp
#include "joystick.h"
#include "rgb_led.h"
#include "color.h"
using namespace drivers;
using namespace common;
Joystick joy(4, 5, 6); // x, y, btn
RgbLed led(3, 10, 2); // r, g, b
void setup() {}
void loop() {
joy.update();
// map X axis 0..200 -> t 0..255
int8_t x = joy.getX(); // -100..+100
uint8_t t = (uint8_t)(x + 100); // 0..200
em_color c = lerp(em_color::RED,
em_color::BLUE, t);
if (joy.wasPressed()) {
led.setColor(em_color::WHITE);
delay(120);
} else {
led.setColor(c);
}
delay(20);
}
Behavior:
Left
LED glows RED
Center
LED is PURPLE (mix)
Right
LED glows BLUE
Press
Flash WHITE briefly
Y axis (getY()) is available but not used in the demo — good extension point for homework!
dead_zone = 10 -> X = 0 near center

## Slide 13
Homework — Lesson 11
Extend the joystick + color system
4

## Slide 14
Lesson 10 — Summary
em_color
Reusable 3-byte color struct in namespace common
Constants
8 named colors as static const members
lerp()
Integer-based color interpolation, no float needed
RgbLed
Extended with setColor(const em_color&) overload
Joystick
Composition: AnalogPin x2 + Button, -100..+100 with dead zone
Composition
Reuse existing drivers classes instead of re-implementing logic
Next: Communication Protocols (I2C, SPI, UART) or further design patterns